## Slide 1: Programmable Measurement Architecture for Data Centers
Minlan Yu
University of Southern California

## Slide 2: Management = Measurement + Control
Trafﬁc engineering, load balancing
  Identify large traffic aggregates, traffic changes
  Understand flow properties (size, entropy, etc.)
Performance diagnosis, troubleshooting
  Measure delay, throughput for individual flows
Accounting
  Count resource usage for tenants
Notes: Management is important, yet underexplored
  Taking 80% of IT budget
  Responsible for 62% of outages
  Measurement is at least half of network management
  Figuring out what’s going on is harder than
  deciding what to do

## Slide 3: Measurement Becoming Increasingly Important
Dramatically expanding data centers
Rapidly changing technologies
Increasing network utilization
Provide network-wide visibility at scale
Monitor the impact of new technology
Quickly identify failures and effects
Notes: Network management is an increasingly important but difficult problem: We need to manage rapidly expand- ing data center infrastructures with rapidly changing network technologies, while achieving many management goals such as high availability, high performance, but low capital and operational expenditures.

## Slide 4: Problems of measurement support in today’s data centers
Notes: What measurement support do today’s DCs provide?

## Slide 5: Lack of Resource Efficiency
Operators:
Passively analyze
the data they have
No way to create the data they want
Network devices:
Limited resources for measurement
Heavy sampling in NetFlow/sFlow
Missing important flows
Too much data with increasing link speed & scale
We need efficient measurement support at devices to create the data we want within resource constraints
Notes: No control of what to measure and what not to measure, devices only have limited resources
No way to generate the data we want

## Slide 6: Lack of Generic Abstraction
Researchers design solutions for specific queries
  Identifying big flows (heavy hitters), flow changes
  DDoS detection, anomaly detection
Hard to support point solutions in practice
  Vendors have no generic support
  Operators write their own scripts for different systems
We need a generic abstraction for operators to program different measurement queries
Notes:   Researchers also take the data they have
Data center brings new opportunities
  to rethink a generic solutions for many queries

## Slide 7: Lack of Network-wide Visibility
Operators manually integrate many data sources
We need to automatically integrate information across the entire network
NetFlow at 1-10K switches
Application logs from 1-10M VMs
Topology, routing, link utilization…
And middleboxes, FPGAs …
Notes: For example, to diagnose performance problems…

## Slide 8: Challenges for Measurement Support
Resource efficiency
(Limited CPU/Mem at devices)
Expressive queries
(Traffic volumes, changes, anomalies)
Network-wide visibility
(hosts, switches)
Our Solution:
Dynamically collect and automatically integrate
the right data, at the right place and the right time

## Slide 9: Programmable Measurement Architecture
Specify measurement queries
Measurement Framework
Dynamically configure devices
Automatically collect the right data
9
Switches
Hosts
FPGAs
Middleboxes
Expressive Abstractions
Efficient runtime
DREAM
(SIGCOMM’14)
OpenSketch
(NSDI’13)
SNAP
(NSDI’11)
FlowTags (NSDI’14)
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 10: Key Approaches
Expressive abstractions for diverse queries
  Operators define the data they want
  Devices provide generic, efficient primitives
Efficient runtime to handle resource constraints
  Autofocus on the right data at the right place
  Dynamically allocate resources over time
  Tradeoffs between accuracy and resources
Network-wide view
  Bring host into the measurement scope
  Tag to trace packets in the network

## Slide 11: Programmable Measurement Architecture
Specify measurement queries
Measurement Framework
Dynamically configure devices
Automatically collect the right data
11
Switches
Hosts
FPGAs
Middleboxes
Expressive Abstractions
Efficient runtime
DREAM
(SIGCOMM’14)
OpenSketch
(NSDI’13)
SNAP
(NSDI’11)
FlowTags (NSDI’14)
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 12: Switches DREAM: dynamic flow-based measurement (SIGCOMM’14)
Notes: Talk about how SNAP helps developers and auto-adaptation

## Slide 13: DREAM: Dynamic Flow-based Measurement
Measurement Framework
13
Switches
Hosts
FPGAs
Middleboxes
Heavy Hitter detection
Change detection
#Bytes=1M
Source IP: 10.0.1.130/31
#Bytes=5M
Source IP: 55.3.4.32/30
Dynamically configure devices
Automatically collect the right data
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 14: Heavy Hitter Detection
Install rules
Fetch counters
Controller
00
13MB
Find src IPs > 10Mbps
01
10
11
13MB
10MB
5MB
Problem: Requires too many TCAM entries
64K IPs to monitor a /16 prefix >> ~4K TCAMs at switches
26
13
13
15
5
10
41
11
10
01
00
Notes: The challenge for using TCAMs is that the number of TCAM entries in switches is limited for power and cost reasons.
We illustrate this using an example measurement task, heavy hitter detection.
Suppose that we are interested in detecting heavy hitters as source IP addresses that send more than 10Mbps.
One way to visualize the traffic from source IP addresses is to use a prefix tree shown on the left.
The numbers inside nodes show the size of their traffic, and the numbers below the leaves show the addresses.
In this prefix tree, we have two heavy hitters in the left subtree.
We can configure rules at switches to monitor all IPs, and periodically fetch counters.
In our example, each switch would have 4 rules, one for each distinct source IP address.
This solution requires too many TCAM entries. [p]
For example, to monitor a large prefix, it needs 64K TCAM entries while today switches have about 4K entries. [p]

## Slide 15
  Key Problem
  How to support many concurrent measurement queries
  with limited TCAM resources at commodity switches?
Notes: So far we have talked about how to find the right configuration of TCAMs for a single task.
But to support many concurrent tasks, we can use other ideas to efficiently use TCAMs.

## Slide 16: Tradeoff Accuracy for Resources
26
13
13
10
5
5
36
11
10
01
00
Monitor internal node to reduce TCAM usage
26
13
13
15
5
10
41
11
10
01
00
Missed heavy hitters
Notes: We can reduce the number of required TCAM entries by monitoring internal nodes in the prefix tree.
In this example, the right subtree has very little traffic, so monitoring the root of the right subtree is enough.
That node has a total traffic of 5, so none of its leaves can be heavy hitters.
The prefix tree on the bottom shows the updated TCAM configuration: this tree now requires only three TCAM entries.

## Slide 17: Diminishing Return of Resource-Accuracy Tradeoffs
Accuracy Bound
82%
7%
Can accept an accuracy bound <100% to save TCAMs
Notes: Changes over traffic and patterns, so we need to estimating the current accuracy
It is possible to be more aggressive in reducing TCAM usage.
We have found a pattern of diminishing returns in accuracy for many measurement tasks.
In this figure, as we double TCAM entries, the accuracy gain becomes smaller and smaller.
Also the additional heavy hitters detected are small and close to the threshold.
So, we can significantly reduce TCAM usage by keeping task accuracy above a bound that is below 100%.

## Slide 18: Temporal Multiplexing across Queries
# TCAMs Required
Time
Query 1
Query 2
Different queries require different TCAMs over time because of traffic changes
Notes: Challenge: moving goal of changing follow the many moving goals tradoeffs of convergence and efficiency
This figure shows how many TCAMs are required for heavy hitter detection task over time.
If two tasks have different TCAM requirements at different times, we can use statistical multiplexing to reduce TCAM usage.
For this, we need to dynamically allocate TCAMs and to reconfigure them.

## Slide 19: Spatial Multiplexing across Switches
Switch A
Switch B
# TCAMs Required
The same query requires different TCAMs at switches because of traffic distribution
Notes: Accuracy of the same query depend on the resources across switches

## Slide 20: Insights and Challenges
Leverage resource-accuracy tradeoffs
  Challenge: Cannot know the accuracy groundtruth
  Solution: Online accuracy algorithm
Temporal multiplexing across queries
  Challenge: Required resources change over time
  Solution: Dynamic resource allocation algorithm rather than one shot optimization
Spatial multiplexing across switches
  Challenge: Query accuracy depends on multiple switches
  Solution: Consider both overall query accuracy and per-switch accuracy
Notes: Management is important, yet underexplored
  Taking 80% of IT budget
  Responsible for 62% of outages
  Measurement is at least half of network management
  Figuring out what’s going on is harder than
  deciding what to do

## Slide 21: DREAM: Dynamic TCAM Allocation
Allocate TCAM
Estimate accuracy
Enough TCAMs  High accuracy  Satisfied
Not enough TCAMs  Low accuracy  Unsatisfied
Notes: The first challenge is dynamic TCAM allocation.
The general idea behind our algorithm is to iteratively and periodically
(a) estimate the instantaneous accuracy of tasks and
(b) adapt TCAM allocation to keep all tasks satisfied.
In this example, suppose that we have two tasks and have estimated their accuracy.
One with happy face has high accuracy and is rich which means it has enough TCAMs,
and another with sad face has low accuracy and is poor.
In the allocation step, we take resources from the rich task and give to the poor one.
Later when tasks measure using the new allocation and we estimate their accuracy, both tasks become satisfied.
In an earlier slide, we showed the curve of the accuracy of measurement vs. the number of allocated TCAMs.
In general, this curve is not known beforehand, and changes with traffic and the specific parameters of a task.
Thus, it is not possible to formulate a one-shot optimization problem for this.
So, we choose an iterative approach.
Second, we don’t know the current accuracy of a task because we don’t have ground truth.
Thus we must estimate accuracy.
I will now describe each of these components.

## Slide 22: DREAM: Dynamic TCAM Allocation
Allocate TCAM
Estimate accuracy
Measure
Online accuracy estimation algorithms based on prefix tree and measurement algorithm
Dynamic TCAM allocation that ensures fast convergence & resource efficiency
Notes: The first challenge is dynamic TCAM allocation.
The general idea behind our algorithm is to iteratively and periodically
(a) estimate the instantaneous accuracy of tasks and
(b) adapt TCAM allocation to keep all tasks satisfied.
In this example, suppose that we have two tasks and have estimated their accuracy.
One with happy face has high accuracy and is rich which means it has enough TCAMs,
and another with sad face has low accuracy and is poor.
In the allocation step, we take resources from the rich task and give to the poor one.
Later when tasks measure using the new allocation and we estimate their accuracy, both tasks become satisfied.
In an earlier slide, we showed the curve of the accuracy of measurement vs. the number of allocated TCAMs.
In general, this curve is not known beforehand, and changes with traffic and the specific parameters of a task.
Thus, it is not possible to formulate a one-shot optimization problem for this.
So, we choose an iterative approach.
Second, we don’t know the current accuracy of a task because we don’t have ground truth.
Thus we must estimate accuracy.
I will now describe each of these components.

## Slide 23: Prototype and Evaluation
Prototype
  Built on Floodlight controller and OpenFlow switches
  Support heavy hitters, hierarchical HH, and change detection
Evaluation
  Maximize #queries with accuracy guarantees
  Significantly outperforms fixed allocation
  Scales well to larger networks

## Slide 24: DREAM Takeaways
DREAM: an efficient runtime for resource allocation
  Support many concurrent measurement queries
  With today’s flow-based switches
Key Approach
  Spatial & Temporal resource multiplexing across queries
  Tradeoff accuracy for resources
Limitations
  Can only support heavy hitters and change detection
  Due to the limited interfaces at switches
Notes: Don’t downgrade dream. Say it’s still important….

## Slide 25: Reconfigurable Devices OpenSketch: Sketch-based measurement (NSDI’13)
Notes: Talk about how SNAP helps developers and auto-adaptation

## Slide 26: OpenSketch: Sketch-based Measurement
Measurement Framework
26
Switches
Hosts
FPGAs
Middleboxes
Heavy hitters
DDoS detection
Flow size dist.
Dynamically configure devices
Automatically collect the right data
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 27: Streaming Algorithms for Individual Queries
How many unique IPs send traffic to host A?
  bitmap
Who’s sending a lot to host A?
  Count-Min Sketch:
# bytes from 23.43.12.1
3
0
5
1
9
0
1
9
3
0
1
2
0
3
4
Hash2
Hash1
Hash3
Data plane
Query: 23.43.12.1
5
3
4
Pick min: 3
Control plane
0
1
0
0
0
1
0
1
0
0
0
0
0
1
0
Hash
Notes:     Bitmap for #unique items, Bloom filter for set member check
  Summarize packet information with Sketches
Not general
  Require customized hardware or network processors
  Hard to implement all solutions in one device

## Slide 28: Generic and Efficient Measurement
Streaming algorithms are efficient, but not general
  Require customized hardware or network processors
  Hard to implement all solutions in one device
OpenSketch: New measurement support at FGPAs
  General and efficient data plane based on sketches
  Easy to implement at reconfigurable devices
  Modularized control plane with automatic configuration

## Slide 29: Flexible Data Plane
Filtering traffic
    (e.g., from host A)
    Classifying a set of flows
    (e.g., Bloom filter for blacklisting IP set)
Picking the packets to measure
Storing & exporting data
Diverse mappings between counters & flows
(e.g., more counters for elephant flows)
Notes: Classification is missing, match on other packet header fields, hash values., and many other data structures

## Slide 30: OpenSketch 3-stage pipeline
# bytes from 23.43.12.1 to host A
3
0
5
1
9
0
1
9
3
0
1
2
0
3
4
Hash2
Hash1
Hash3
Notes: Classification is missing, match on other packet header fields, hash values., and many other data structures

## Slide 31: Build on Existing Switch Components
Simple hash function
Traffic diversity adds randomness
Only 10-100 TCAMs after hashing
Logical tables with flexible sizes
SRAM counters accessed by addresses

## Slide 32: Example Measurement tasks
Heavy hitter detection
  Who’s sending a lot to host A?
  count-min sketch to count volume of ﬂows
  reversible sketch to identify ﬂows with heavy counts in the count-min sketch
# bytes from host A
CountMin Sketch
Reversible Sketch

## Slide 33: Support Many Measurement Tasks
Measurement Programs | Building blocks | Line of Code
Heavy hitters | Count-min sketch; Reversible sketch | Config:10 Query: 20
Superspreaders | Count-min sketch; Bitmap; Reversible sketch | Config:10 Query:: 14
Traffic change detection | Count-min sketch; Reversible sketch | Config:10 Query: 30
Trafﬁc entropy on port ﬁeld | Multi-resolution classiﬁer; Count-min sketch | Config:10 Query: 60
Flow size distribution | multi-resolution classiﬁer; hash table | Conﬁg:10 Query: 109

## Slide 34: OpenSketch Prototype on NetFPGA

## Slide 35: OpenSketch Takeaways
OpenSketch: New programmable data plane design
  Generic support for more types of queries
  Easy to implement with reconfigurable devices
  More efficient than NetFlow measurement
Key approach
  Generic abstraction for many streaming algorithms
  Provable resource-accuracy tradeoffs
Limitations
  Only works for traffic measurement inside the network
  No access to application level information

## Slide 36: Hosts SNAP: Profiling network-application interactions (NSDI’11)
Notes: Talk about how SNAP helps developers and auto-adaptation

## Slide 37: SNAP: Profiling network-application interactions
Measurement Framework
37
Switches
Hosts
FPGAs
Middleboxes
Perf. diagnosis
Workload monitoring
Dynamically configure devices
Automatically collect the right data
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 38: Challenges of Datacenter Diagnosis
Large complex applications
  Hundreds of application components
  Tens of thousands of servers
New performance problems
  Update code to add features or ﬁx bugs
  Change components while app is still in operation
Old performance problems (Human factors)
  Developers may not understand network well
  Nagle’s algorithm, delayed ACK, etc.
Notes: We have many low-level protocols such as….that is a mystery to developers without a networking background, but these protocols may have significant performance impact. It could be a disaster for a database expert to work with a TCP stack
- slide 34: audience probably won't know what "Nagle's algorithm" and "delayed ACK" are. you can finesse this out loud, and say that networking protocols have many low-level mechanisms (and view these as examples you don't expect the audience to know).
in practice, I think Microsoft doesn't
really "hot swap" in the new code, but rather brings up new images for a
service and gradually phase out the old ones your point is more that change
in constant.
Just stress the point about constant influx of new developers out loud.
silly window syndrome

## Slide 39: Diagnosis in Today’s Data Center
Host
App
OS
Packet sniffer
Application logs:
#Requests/sec
Response time
1% req. >200ms delay
Switch logs:
#bytes/pkts per minute
Packet trace:
Filter out trace for long delay req.
SNAP:
Diagnose net-app interactions
Application-specific
Too expensive
Too coarse-grained
Generic, fine-grained, and lightweight
Notes: Google and microsoft
100K$ a few monitoring machines monitor two racks of servers

## Slide 40: SNAP: A Scalable Net-App Profiler that runs everywhere, all the time

## Slide 41: SNAP Architecture
Management System
At each host for every connection
Collect data
Performance Classifier
Cross-connection correlation
Adaptively polling per-socket statistics in OS
Snapshots (#bytes in send buffer)
Cumulative counters (#FastRetrans)
Classifying based on the stages of data transfer
Sender appsend buffernetworkreceiver
Topology, routing
Conn  proc/app
Offending app,
host, link, or switch
Online, lightweight processing & diagnosis
Offline, cross-conn diagnosis
Notes: Overview to give sense of what SNAP is
Tuning polling rate to reduce overhead
Input
  Topology, routing information
  Mapping from connections to processes/apps
  Sharing the same switch/link, app code

## Slide 42: Programmable SNAP
Virtual tables at hosts
  Lazy update to the controller
App CPU usage,
App mem usage,
…
#Bytes in send buffer,
#FastRetrans
…
SQL like query language at the controller
def queryTest():
q = (Select(‘app’, ‘FastRetrans’) *
From('HostConnection') *
Where(('app','==',’web service’)) *
Every(5 mintue))
return q

## Slide 43: SNAP in the Real World
Deployed in a production data center
  8K machines, 700 applications
  Ran SNAP for a week, collected terabytes of data
Diagnosis results
  Identified 15 major performance problems
  21% applications have network performance problems
Notes: Terabytes , less than 1 GB per machine per day
Read every 500 ms
700 always running, persistent connection
> - summarize that you found 15 serious performance bugs and worked with
developers to fix their code.

## Slide 44: Characterizing Perf. Limitations
Send Buffer
Receiver
Network
#Apps that are limited for > 50% of the time
1 App
6 Apps
8 Apps
144 Apps
  Send buffer not large enough
  Fast retransmission
  Timeout
  Not reading fast enough (CPU, disk, etc.)
  Not ACKing fast enough (Delayed ACK)
Notes:   6 apps self inflicted packet loss" "incast
  Life of transfer: be sure to talk about ack
  One connection is always limited by one component, it’s good for the network, if it’s limited by apps
  Nagle and delayed ack… : small data which trigger Nagle’s algo.

## Slide 45: SNAP Takeaways
SNAP: Scalable network-application profiler
  Identify performance problems for net-app interactions
  Scalable, lightweight data collection at all hosts
Key approach
  Extend network measurement to end hosts
  Automatic integration with network configurations
Limitations
  Require mappings of applications and IP addresses
  Mappings may change with middleboxes

## Slide 46: FlowTags: Tracing dynamic middlebox actions
Measurement Framework
46
Switches
Hosts
FPGAs
Middleboxes
Performance diagnosis
Problem attribution
Dynamically configure devices
Automatically collect the right data
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 47: Modifications  Attribution is hard
S1
S2
Firewall
NAT
Internet
Block H1: 192.168.1.1
Block H3: 192.168.1.3
FW Config in terms of original principals
H1 192.168.1.1
H2
192.168.1.2
H3
192.168.1.3
Middleboxes modify packets
Goal: enable policy diagnosis and attribution
despite dynamic middlebox behaviors

## Slide 48: FlowTags Key Ideas
Middleboxes need to restore SDN tenets
  Strong bindings between a packet and its origins
  Explicit policies decide the paths that packets follow
Add missing contextual information as Tags
  NAT gives IP mappings
  Proxy provides cache hit/miss info
FlowTags controller configures tagging logic

## Slide 49: Walk-through example of end system
S1
S2
FW
NAT
Internet
H1 192.168.1.1
H2
192.168.1.2
H3
192.168.1.3
SrcIP | Tag
192.168.1.1 | 1
192.168.1.2 | 2
192.168.1.3 | 3
Tag | OrigSrcIP
1 | 192.168.1.1
3 | 192.168.1.3
NAT Add Tags
FW Decode Tags
Tag | Forward
1,3 | FW
2 | Internet
S2 FlowTable
Tag Generation
Tag Consumption
Tag Consumption
Block H1: 192.168.1.1
Block H3: 192.168.1.3
FW Config in terms of original principals
Notes: We have three hosts H1 − H3 private address space; the ad- ministrator wants to block Internet access for H1, H3, and allow H2’s packets to pass through without going to the firewall. The controller (not shown) configures the NAT to associate outgoing packets from H1 , H2 , and H3 with
the Tags 1, 2, and 3, respectively, and add these to pre- specified header fields. (See §5.3). The controller configures the firewall so that it can decode the Tags to map the observed IP addresses (i.e., in “public” address space using RFC1918 terminology) to the original hosts, thus meeting the ORIGINBINDING requirement. Similarly, the controller configures the switches to allow packets with Tag 2 to pass through without going to the firewall, thus meeting the PATHSFOLLOWPOLICY requirement. As an added benefit, the administrator can configure fire- wall rules w.r.t. the original host IP addresses, without needing to worry about the NAT-induced modifications.

## Slide 50: FlowTags Takeaways
FlowTags: Handle dynamic packet modifications
  Support policy verification, testing, and diagnosis
  Use tags to record packet modifications
  25-75 lines of code changes at middleboxes
  <1% overhead to middlebox processing
Key approach
  Tagging at one place for attribution at other places

## Slide 51: Programmable Measurement Architecture
Specify measurement queries
Measurement Framework
Dynamically configure devices
Automatically collect the right data
51
Switches
Hosts
FPGAs
Middleboxes
Expressive Abstractions
Efficient runtime
DREAM
Flow counters
OpenSketch
New measurement pipeline
SNAP
TCP & socket statistics
FlowTags
Tagging APIs
Traffic measurement inside the network
Performance Diagnosis
Attribution
Notes: Operators first specify…
My research focuses on how to redesign the network to address the three challenges at the same time. I built two systems:
Due to the three challenges, today, network operators devote tremendous time and effort to network management.
Yankee group reports that in enterprises 80% of IT budget is spent on network management.
But they can only support a limited management tasks.
I built two new systems that make the network more scalable and easier to manage.
Focus on DIFANE, and give a brief description of SNAP
How to design network functions that best support different management tasks
How to implement different management tasks in the network

## Slide 52: Extending Network Architecture to Broader Scopes
Measurement
Control
Network Devices
Abstractions for programming different goals
Algorithms to use limited resources
Integrations with the entire network
Notes: Measurement is as important as control in network devices

## Slide 53: Thanks to my Collaborators
USC: Ramesh Govindan, Rui Miao, Masoud Moshref
Princeton
  Jennifer Rexford, Lavanya Jose, Peng Sun, Mike Freedman, David Walker
CMU: Vyas Sekar, Seyed Fayazbakhsh
Google: Amin Vahdat, Jeff Mogul
Microsoft
  Albert Greenberg, Lihua Yuan, Dave Maltz, Changhoon Kim, Srinkath Kandula