## Slide 1: S-NIC: Securing NIC-Accelerated Network Functions in the Cloud
Yang Zhou, Mark Wilkening, James Mickens, Minlan Yu
Harvard University
Notes: Hi everyone, my name is Mark Wilkening. I’ll be presenting today on behalf of my colleague Yang Zhou, for our work (securing... ). This project, S-NIC, is a joint collaboration between Yang and myself, and his advisors, professors Mickens and Yu from Harvard University.

## Slide 2: Network Functions (NFs) are popular
Network Functions (NFs) are critical infrastructure in networked systems.
  Firewall, NATs, WAN optimizers, deep packet inspection (DPI), etc.
NAT
WAN
Snort3 DPI
Notes: Before I delve into our design, I’ll motivate our work by first asserting that network functions are critical infrastructure in networked systems, for example, Firewall, NATs, WAN optimizers, deep packet inspection (DPI), etc.
These NFs manipulate each incoming packet, including header or payload or both, and then forward or drop the packet.
Previously, these NFs are running in company-owned on-premise hardware middleboxes or servers, which is hard to evolve or maintain.

## Slide 3: NF Outsourcing to the Cloud
  Scale on demand as the traffic load changes  Cheaper!
  Easier to manage, upgrade, and deploy. Outsourcing these tasks
Client
Enterprise
Server
Dest.
Enterprise
Server
Email
Two key requirements: Performance and Security
Notes: With the growth of cloud services, enterprise institutions have begun to outsource NFs to the cloud, as cloud NFs can scale on demand and are easier to manage, upgrade, and deploy.
Like many other workloads, when running network functions on the cloud there are two key requirements, performance and security.

## Slide 4: Requirement: High Performance
Achieving high performance is important but challenging.
  High performance to keep up with link speed (10/40/100Gbps) as traffic grows.
  Microsoft AccelNet [NSDI’18]:
“We got a 50x improvement in network throughput,
but not a 50x improvement in CPU power!”
Notes: First, let’s go over performance. Achieving high performance is actually quite difficult. Performance requirements scale with increasing link speed, which has jumped from 1G to 10G then 40G, and 100G.
As a somewhat recent study from Microsoft azure has pointed out, the drastic rate of improvement in network throughput capabilities is not scaling commensurately with CPU performance. “We got a fifty times improvement in network throughput, but not a fifty times improvement in CPU power”.
So, It becomes harder and costly if we keep running all the NFs on CPU cores.

## Slide 5: Today: Running NFs on VMs
Low performance:
Firewall = 0.66Gbps/core
(NetBricks [OSDI’16])
Hypervisor
NF
VM
NF
VM
NF
VM
NF
VM
Hardware
Virtualization Overhead
+
Not secure:
Even Intel SGX still suffers from
Notes: For many enterprise customers, NFs run on top of VMs on commodity servers.
In terms of performance, a recent study shows that a typical firewall can only achieve 0.66Gbps per core on bare metal commodity server.
Besides, you also needs to pay the virtualization overhead caused by running hypervisor and various management software..
In terms of security, even TEE’s such as intel SGX, still rely on an untrusted OS to perform I/O.
Intel SGX also suffers from various side-channel attacks.
-------------------------------------------------------------------
What’s the virtualization overhead?
https://meltdownattack.com/

## Slide 6: An Alternative: Running NFs on Smart NICs
Azure is offloading their full cloud storage stack to multi-core Smart NICs1.
Available NICs: Mellanox BlueField, Broadcom Stingray, Marvell LiquidIO, etc.
NF
Core
NF
core
NF
core
NF
core
Bad Security:
  No mem. isolation
  No perf. isolation
SmartNIC
Traffic
Good efficiency:
  Cost-efficient RISC cores
  ASIC-based accelerators
  No PCIe traversing
1 Li, Huaicheng, et al. "LeapIO: Efficient and Portable Virtual NVMe Storage on ARM SoCs." ASPLOS 2020.
Notes: As an alternative solution, cloud can run NFs in a smart NIC. Smart NIC is one type of network interface card that has programmable cores or FPGA attached.
These cores and FPGA can be programmed to manipulate the incoming packets.
Actually, Azure is offloading their full cloud storage stack to multi-core smart NICs as it is easier to program, manage, and rapidly build, compared with FPGA.
Available commodity smart NIC includes: Mellanox BlueFiled, Broadcom stringray, Marvell LiquidIO, etc. In this talk, we will focus on multi-core smart NIC.
So, the benefit of running NFs in a multi-core smart NIC is the good efficiency it provides, as these NICs have cost-efficient RISC cores with low power consumptions, they also have ASIC-based accelerators built in for various packet processing functionalities, such as pattern matching used in DPI. Also, by running NFs in NIC, the PCIe traversing latency is avoided.
However, there are also some drawbacks of existing mutli-core smart NICs. For example, there is no effective memory isolation and performance isolation which we cover in more detail in the paper.

## Slide 7: S-NIC Redesign Smart NICs to provide high performance and strong security for network functions
Notes: So we present S-NIC, a redesign of existing smart NICs to provide cloud-based network functions with
both high performance and strong isolation.

## Slide 8: Background on (Multi-Core) Smart NICs
Memory: DRAM, SRAM
Hardware accelerators
Packet ingress and egress
IO bus
Smart NICs are not designed for shared environment
Notes: Before going deep into S-NIC’s hardware design, let’s get a brief overview of how existing multi-core smart NICs look like.
So, this diagram shows the high-level components of one typical commodity smart NIC,
including dozens of programmable cores mostly in ARM or MIPS architecture, memory, hardware accelerators, packet ingress and egress, which are connected by an internal IO bus.

## Slide 9: Threat Model
OS
Core
SmartNIC
Trusted: NIC Hardware
NF
core
NF
core
NF
core
Goals:
1) Isolation
2) Side-channel-free
(shared HW states)
Out of scope:
Physical possession attacks
DoS attacks from Cloud
Notes: The threat model of S-NIC is that we only trust the NIC hardware, while the management software or the NIC OS running on the smart NIC cores is malicious, the NFs from the other users running in the same NIC are also malicious.
So our goal is, first, isolating an NF from NIC OS and other NFs running on the NIC, second, eliminating side channels involving shared hardware state such at cache, memory bus.
The physical possession attacks and denial-of-service attaches from the cloud are out of scope of our thread model; S-NIC can leverage preexisting techniques to thwart such out-of-scope attacks.
--------------------------------------------------------------
// Is this the same as SGX threat model or different?
We want to do a bit more than SGX -- Eliminating side channels involving shared hardware state
NFShield leverages preexisting techniques to thwart such out-of-scope attacks.
If the NIC is connected to the host
  Trusted computing base: + host enclave hardware
  But not trust the host software
----------------------------original slide
Trusted computing base:
  NIC hardware
Goal:
  Isolating an NF from NIC OS and other NFs running on the NIC
  Eliminating side channels involving shared hardware state
Out of scope:
  Physical possession attacks (e.g., memory bus tapping)
  Denial of service attacks from the cloud

## Slide 10: S-NIC: Key Designs
Single-owner RAM Semantics
Bus Arbitration
Accelerator Virtualization
Packet IO Virtualization
Notes: So here we show the overall architecture of S-NIC.
SNIC does not provide the same level of flexibility as the virtualization available in a general-purpose multi-core server and operating system. In S-NIC we need to thoroughly isolate entire virtual packet pipelines, including programmable cores, memory, fixed-function accelerators, and I/O hardware, and we require both architectural and microarchitectural isolation between both running functions and the management software.
This leads us to require strict partitioning of resources between virtual network functions as well as the management software. The management core can still make resource partitioning and allocation decisions between virtual functions, but there can be no on-the-fly adjustments to running network functions besides termination.
S-NIC introduces four key design elements: single-owner RAM semantics, accelerator virtualization, packet IO virtualization, and bus arbitration.

## Slide 11: S-NIC: Key Designs
Single-owner RAM Semantics
Bus Arbitration
Accelerator Virtualization
Packet IO Virtualization
Notes: Let first see the single-owner RAM semantics.

## Slide 12: Design: Single-Owner RAM Semantics
Goals:
  Prevent NFs from accessing other NF’s memory.
  Prevent OS from accessing arbitrary memory.
  Prevent side channels in cache.
Solution – single-owner RAM semantics
  A RAM region exclusively belongs to either a running network function, or to the management OS.
Notes: So we have three goals in mind: first, prevents NFs from accessing other NF’s memory, second, preventing OS form accessing arbitrary memory, and third preventing side channels in the shared cache.
These three goals regarding the RAM resource motivate us to enforce single-owner RAM semantics, which means a RAM region exclusively belongs to either a running network function, or to the management OS.
The first goal is relatively simple and uses existing memory virtualization technology such as virtual paging and TLBs for NF cores. The difficulty arises when trying to protect assigned regions from the operating system which is involved in setting up and managing these translations.

## Slide 13: Preventing OS from modifying Translations
No (modifyable) page table for programmable cores.
  Preventing NFs and OS from manipulating the mapping.
  As the cost of constraining the memory an NF can use.
  NF profiling shows: common NFs require < 70MB memory
nf_launch installs TLBs with memory mapping on each programmable core.
  Once nf_launch completes, the hardware sets the TLBs to read-only
  Common NFs require < 40 TLB entries (2MB page)
NF0
NF1
OS
Notes: We introduce explicit nf_launch and nf_teardown ISA instructions to create and terminate network functions. These are run using microcode in the MMU and restrict the operating system from modifying the translations of running functions.
Because typically network functions require small memory allocations, we choose to have nf_launch directly configure translations within the hardware TLBs. An alternate design using conventional page table pointers can also be used by having nf_launch force the page table memory itself to be read only during NF execution.

## Slide 14: Preventing OS using Blacklist Page Table
OS
Core
NF0
core
NF1
core
RAM
P1
P2
P3
P1,
P2,
P3,
nf_launch
Use trusted hardware instruction nf_launch:
Blacklist NF RAM pages and configurations on the OS core
Notes: To prevent the management core from accessing the memory of launched network functions, we introduce a blacklist page table, configured by nf_launch.
On a page-fault in the management core, the MMU will obtain the virtual page translation of the address through a conventional page table walk, but additionally will then perform a walk of the blacklist page table to determine exclusivity rights.
This mechanism is like Extended Page Tables (EPT) used for shadow paging and can use the same hardware optimizations.

## Slide 15: S-NIC: Key Designs
Single-owner RAM Semantics
Bus Arbitration
Accelerator Virtualization
Packet IO Virtualization
Notes: The final key design of NFShield is bus arbitration to avoid any side channels caused by bus contention.

## Slide 16: S-NIC: Key Designs
Single-owner RAM Semantics
Bus Arbitration
Accelerator Virtualization
Packet IO Virtualization
Notes: So far, we have gone through how NFshield handles RAM isolation via single-owner RAM semantics.
Now, let’s talk about how NFSheild virtualizes hardware accelerators in a securely manner.

## Slide 17: A. Clustering Threads with TLB Banks
S-NIC partitions threads and RAM into multiple clusters (vDPIs)
  Avoid context switching to get high performance.
Each vDPI has a TLB banks with appropriate memory mappings.
Notes: So our choice in NFshield is to partition these hardware threads and RAM into multiple clusters, this avoid context switching for high performance.
For example, in this diagram, we have multiple vDPIs, and each vDPI has its own on-accelerator cache and DRAM regions for DPI graph and instruction queue.
Each vDPI also has a TLB bank with appropriate memory mappings to constrain its memory accessing behavior.
Each vDPI as a whole is allocated to one NF at a time for use.
----------------------------------------------------------------
We could do time sharing but it takes a lot of overhead, or dynamic thread allocation

## Slide 18: S-NIC: Key Designs
Single-owner RAM Semantics
Bus Arbitration
Accelerator Virtualization
Packet IO Virtualization
Notes: So, the third design of NFshield is the packet IO virtualization.

## Slide 19: Evaluation: Hardware Cost (TLB entries)
  Use standard open source NFs with real traffic setting
    Take the largest memory, accelerator, virtual packet pipeline requirements
  Use the McPAT modeling framework to generate hardware cost estimates,
  Compare to an ARM Cortex-A9 multicore processor (a relatively small processor).
 | TLBs for programmable cores | TLBs for virtualized accelerators | TLBs for packet IO
Chip area (mm^2) | 0.163 | 0.091 | 0.074
Power (W) | 0.088 | 0.044 | 0.034
8.89% chip area and 11.45% power.
Notes: The major hardware cost of NFShield comes from the use of TLB entries for programmable core, virtualized accelerators, and packet IO,
The blacklisting logic has small costs as it can be implemented similar to extended page table.
Bus arbiters also have small cost, as from the original paper.
In terms of TLB entries, we use standard open source NFs with real traffic setting to estimate the largest memory, accelerator and virtual packet pipeline requirements, and thus get the largest number of required TLB entries.
We use the McPAT modeling framework to generate hardware cost estimates, and compare to an ARM Cortex-A9 multicore processor.
Results show around 8.89% chip area and 11.45% power increase compared with the ARM Cortex-A9, which is a fairly modest hardware overhead.

## Slide 20: Evaluation: Performance
Gem5 models Marvell LiquidIO NIC cores, cache, memory, and bus with:
  Static partitioning for the cache.
  Temporal partitioning for the bus.
Runs six NFs
  Firewall (FW), DPI, NAT, Load Balancer (LB), LPM, Monitor (Mon)
We measured the instructions-per-cycle (IPC) degradation.
  Directly reflecting function throughput reduction.
Notes: In terms of performance evaluation, we use GEM5 hardware simulator to model Marvell LiquidIO NIC cores, cache, memory and bus.
We focus on the performance impact of static partitioning for the cache, and temporal partitioning for the bus.
The other overhead such as nf_launch latency and TLB entries do not impact or has very little impact on the performance of running NFs.
We run six NFs, and measure their instructions-per-cycle, the IPC degradation, which directly reflects function throughput reduction.

## Slide 21: Evaluation: Performance
Cache partitioning, and bus arbitration reduce function throughput by less than 13.71% in the worst case.
Notes: The results shows that with cache partitioning and bus arbitration, NF throughput is reduces by less than 13.71% in the worse case.
Thus, NFShield preserves the traditional performance benefits of function offloading.

## Slide 22: Conclusion
Outsource NFs to the cloud requires high performance and strong security, and offloading to smart NIC is an attractive option.
S-NIC redesigns smart NICs to provide strong isolation with modest hardware overheads, while preserving performance benefits of smart NICs.
S-NIC achieves both by
  enforcing single-owner semantics for on-NIC RAM and caches,
  pervasively virtualizing hardware accelerators and packet IO,
  providing dedicated bus bandwidth for each NF
Notes: Let’s draw conclusion now.
Outsourcing NFs to the cloud requires high performance and strong security, and offloading to smart NIC is an attractive option.
NFShield redesigns smart NICs to provide strong isolation with modest hardware overheads, while preserving performance benefits of smart NICs.
NFShield achieves both by enforcing single-owner semantics for on-NIC RAM and caches,
pervasively virtualizing hardware accelerators and packet IO, and providing dedicated bus bandwidth for each NF

## Slide 23
Thanks!
Q&A
Notes: Here ends my talk, thanks for your time to attend my qualifying exam. I am happy to take any questions.