## Slide 1: Your network doesn’t end at the NIC
A case for unifying the inter-host and intra-host networks in (AI) datacenters
Raj Joshi†, Saksham Agarwal‡, ChonLam Lao†, Minlan Yu†
†Harvard University, ‡UIUC

## Slide 2: Network layer Ethernet/IP stack started/ended at NIC
Host A
Host B
10.1.1.1
20.1.1.1
Notes: Traditionally, the network layer of Ethernet/IP stack has always begun and ended at the NIC
The network layer first assigns addresses to the NIC interfaces
Then provides the routing of packets from between the NICs

## Slide 3: Network layer of Ethernet/IP stack ends at the NIC
Host A
Host B
10.1.1.1
20.1.1.1
PCIe
PCIe
Memory Bus
Memory Bus
App/OS buffers
App/OS buffers
Worked well for ~2 decades for traditional datacenter workloads
Run completely different network protocols
Data transfers
Notes: Within the host, the network is simple
The NIC connects to the CPU I/O over PCIe and then to the DRAM via the memory bus.
The network protocols of the memory bus, PCIe interconnect, Ethernet/IP network work independently of each other.
But together they enable data transfers between the app/OS buffers residing on the DRAM.
This has worked well for traditional server/client …

## Slide 4: Two paradigm shifts driven by modern workloads such as LLMs
Notes: However, there have been 2 main shifts from the status quo driven by modern …

## Slide 5: Multi-GPU servers: large, complex intra-host networks
Notes: First is that, today we have multiple GPU servers with large and complex intra-host networks
These servers have up to 8 GPUs connected via intra-host GPU fabric
GPUs are also connected to multiple RDMA NICs, SSDs, and DRAM via a large PCIe fabric consisting of multiple PCIe switches

## Slide 6: Data transfers in today’s ML workloads
Data transfers are between App/OS buffers (on the DRAM)
Traditional Workloads
More peer-to-peer transfers between intra-host devices (performance reasons)
LLM Workloads
Notes: Second paradigm shift is that, unlike traditional workloads ... where data transfers are between
today’s LLM workloads involve more P2P data transfers between intra-host devices

## Slide 7: Workloads: P2P transfers between intra-host devices
GPU ↔ GPU
Notes: GPUs directly communicate with each other over the intra-host GPU fabric

## Slide 8: Workloads: P2P transfers between intra-host devices
GPU ↔ CPU Memory
Notes: GPUs directly communicate with the CPU memory

## Slide 9: Workloads: P2P transfers between intra-host devices
GPU ↔ SSDs (GPUDirect Storage)
Notes: They also communicate with directly with local SSDs

## Slide 10: Workloads: P2P transfers between intra-host devices
GPU ↔ RNIC ↔ remote GPUs/memory/SSDs
Notes: They communicate with the RNICs to in order to directly reach remote GPUs/memory/SSDs

## Slide 11: Protocols for the intra- and inter-host networks have not evolved in response to these paradigm shifts!
The Problem
Notes: The problem is that

## Slide 12
Example: Collective Communication in distributed LLM Training
Typically involves 100s to 1000s of GPUs
To understand WHY this is a problem
Notes: To understand WHY this is a problem, let’s take an example of distributed LLM training

## Slide 13: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
Notes: The figure here shows a single step in collective comm, where GPU_A0 in server A sends data to GPU_B0 in server B

## Slide 14: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
Both GPUs register a memory buffer with nearest RNICs
Notes: The way it works is as following:
  Both GPUs register a memory buffer with their nearest RNICs

## Slide 15: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
RNIC_A0 reads data from GPU_A0, sends RDMA Write pkts. RNIC_B0 writes to GPU_B0.
PCIe Read
PCIe Cmpl
RDMA Write
PCIe Write
Notes: Then RNIC_A0 reads data from GPU_A0 …

## Slide 16: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
Consider a case where RNIC_B0 fails!
PCIe Read
PCIe Cmpl
RDMA Write
PCIe Write

## Slide 17: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
If RNIC_B0 fails, then GPU_B0 becomes unavailable!
PCIe Read
PCIe Cmpl
RDMA pkts
PCIe Write
Training stalls immediately!
~11 mins of total downtime. ~5 mins wasted GPU compute.
Impact even greater at larger scales.
      (more details in the paper)

## Slide 18: Single step in Collective Communication
GPU_A0 (server A) sends data to GPU_B0 (server B) via GPUDirect RDMA
Inter-host network: RDMA over Ethernet
Core issue: loss of connectivity to GPU_B0, despite alternative paths.
PCIe Read
PCIe Cmpl
RDMA Write
PCIe Write
But today’s intra- and inter-host network protocols do NOT support using the alternative path!
2 reasons
Notes: The core issue here is the loss of connectivity to GPU_B0, despite having alt paths e.g. the blue path that shows that we can reach GPU_B0 through RNIC_B7 and GPU_B7

## Slide 19: Intra- and Inter-host networks operate independently
Inter-host network: RDMA over Ethernet
Inter-host network ends at the RNIC and has no visibility beyond it!
  Writing to GPU_B0 Writing to RNIC_B0. Unaware of the blue path via RNIC_B7.
RDMA Write
End-to-End Routing Problem
Notes: The 1st reason is that the intra and inter-host networks operate independently
As a result, the inter-host network ends at the RNIC and has no visibility beyond it.
From the inter-host network’s perspective, writing to GPU_B0 is basically abt writing to RNIC_B0.
We call this end-to-end routing problem

## Slide 20: Intra-host: rudimentary point-to-point protocols
Inter-host network: RDMA over Ethernet
Limited support for forwarding across heterogenous interconnects
  e.g. for blue path to work, PCIe Writes need to be forwarded by GPU_B7 over GPU fabric
RDMA Write
??
Intra-host Forwarding Problem
Notes: The 2nd reason is that the intra-host network runs rudimentary point-to-point protocols
With limited support for forwarding across heterogenous interconnects
e.g. for the blue path to work, PCIe writes need to be forwarded to

## Slide 21: To better support device-to-device communication
We need to re-architect the AI datacenter network to treat intra-host devices as the ultimate network endpoints.
Paradigm: the intra-host and inter-host networks operate together as a single, unified network.
Notes: To solve these problems and to better support device-to-device communication
to this end, we envision a paradigm where …

## Slide 22: Blueprint for realizing this vision
Uniquely identifies intra-host devices across the datacenter
Global Addressing Scheme
Routes across the intra- and inter-host networks
Unified Routing Scheme
Forwarding Mechanism
Bridges different intra-host interconnects
Notes: We outline a blueprint for realizing this vision, which comprises of
… Iet’s take a quick look into these through our LLM training example

## Slide 23: Global Addressing Scheme
Each intra-host device has unique DeviceID: ServerID + LocalDeviceID
11.17.3.2
ServerID:
22
LocalDeviceID
  GPU_B0 DeviceID: 11.17.3.2:22
Notes: For each server we first assign a ServerID. e.g. server B is assigned 11.17.3.2. This can something like an IP address.
Within each server, each device is assigned a DeviceID e.g. GPU_B0 is assigned 22

## Slide 24: Unified Routing Scheme
11.17.3.2
ServerID:
22
Local Routing Agent
Local Routing Agent
Centralized Routing Controller
intra-host routes and costs
Notes: Now, for unified routing, a local routing agent reports intra-host routes and costs to a centralized routing controller

## Slide 25: Unified Routing Scheme
11.17.3.2
ServerID:
22
Centralized Routing Controller
11.17.3.2:22 | via RNIC_A0
11.17.3.2:22 | ECMP(spine)
11.17.3.2:22 | fwd(L24)
11.17.3.2:22 | fwd(port_GPU_B0)
End-to-End datapath: GPU_A0 to GPU_B0
Notes: Which then installs the rules across the intra- and inter-host networks thereby establishing an end-to-end datapath between..
Note that the routing rules are also installed on intra-host devices including the GPUs and the PCIe switches
And all switching devices including Ethernet switches match on the globally unique device ID of GPU_B0

## Slide 26: Unified Routing Scheme
11.17.3.2
ServerID:
22
Centralized Routing Controller
11.17.3.2:22 | via RNIC_A0
11.17.3.2:22 | ECMP(spine)
11.17.3.2:22 | fwd(L24)
11.17.3.2:22 | fwd(port_GPU_B0)
Notes: Now, when RNIC_B0 fails, the local routing agent informs the same to the centralized routing controller, which then updates the routing rules

## Slide 27: Unified Routing Scheme
11.17.3.2
ServerID:
22
Centralized Routing Controller
11.17.3.2:22 | via RNIC_A0
11.17.3.2:22 | ECMP(spine)
11.17.3.2:22 | fwd(L31)
11.17.3.2:22 | fwd(port_GPU_B7)
Notes: to use the alternative path via RNIC_B7 and GPU_B7

## Slide 28: Unified Routing Scheme
11.17.3.2
ServerID:
22
Centralized Routing Controller
11.17.3.2:22 | via RNIC_A0
11.17.3.2:22 | ECMP(spine)
11.17.3.2:22 | fwd(L31)
11.17.3.2:22 | fwd(port_GPU_B7)
Q. How does GPU_B7 forward data from its PCIe interface to its GPU fabric interface?
??
Forwarding Mechanism
Bridges PCIe and GPU Fabric interconnects (more details in the paper)
Notes: But one question still remains: how does …
That’s where our blueprint’s forwarding mechanism comes into picture that bridges PCIe and …

## Slide 29: Unified Routing Scheme
11.17.3.2
ServerID:
22
Centralized Routing Controller
11.17.3.2:22 | via RNIC_A0
11.17.3.2:22 | ECMP(spine)
11.17.3.2:22 | fwd(L31)
11.17.3.2:22 | fwd(port_GPU_B7)
Network-layer can re-route around failures!
Allowing current iteration to complete.
Reducing downtime and GPU compute wastage
Distributed LLM Training Scenario
Notes: What this means for our distributed LLM training scenario is

## Slide 30: Supporting emerging device-to-device communication
Proposed
Blueprint
Foundational Datagram Service
Addressing, routing, and forwarding
End-to-End Semantics
Reliability and Congestion Control
Security and Isolation
Firewall and ACLs, QoS
First step!
Foundation
for a rich
future
research
agenda!
Notes: Now zooming out, in the grand scheme of supporting …, our proposed blueprint provides a framework for a foundational datagram service that provides addressing, routing and forwarding.
But it is truly just the first step!
More importantly, it lays the foundation for a rich research agenda, with exciting questions from designing new end-to-end semantics for reliability and congestion control to ensuring robust security and isolation.

## Slide 31: Supporting emerging device-to-device communication
New Industry Standards
Help shape the future of device-to-device communication
Notes: With new industry standards like UALink and UltraEthernet already emerging, now is the perfect time for us, the research community, to help shape the future of device-to-device communication.

## Slide 32: Thank you!
Credits: This presentation template was adapted from Slidesgo, including icons by Flaticon.
Flaticon icons by: Freepik, Muhammad_Usman, Paul J., IconMarketPK, Awicon, Pixel perfect, Eucalyp, andinur, Uniconlabs, Nikita Golubev, Konkapp, Iconjam, Flat Icons, Uniconlabs, RaftelDesign, wanicon, Design Circle, Iconjam, Smashicons, Iconjam, Uniconlabs, pojok d, ultimatearm.

## Slide 33: Supporting emerging device-to-device communication
Proposed
Blueprint
Foundational Datagram Service
Addressing, routing, and forwarding
End-to-End Semantics
Reliability and Congestion Control
Security and Isolation
Firewall and ACLs, QoS
First step!
Foundation
for a rich
future
research
agenda!
Notes: Now zooming out, in the grand scheme of supporting …, our proposed blueprint provides a framework for a foundational datagram service that provides addressing, routing and forwarding.
But it is truly just the first step!
More importantly, it lays the foundation for a rich research agenda, with exciting questions from designing new end-to-end semantics for reliability and congestion control to ensuring robust security and isolation.

## Slide 34: Why not do it at the application-layer?
Context: LLM Training RNIC failure & forwarding via transit GPU_B7
Requires a staging buffer on the transit GPU (extra data copy!)
  Consumes valuable memory on the transit GPU
  Requires complex mechanisms to avoid interfering with GPU’s local workloads
Huge control overhead in doing a “chunked” pipelined transfer
  Send a chunk to GPU_B7 via RNIC_B7  pipelined memcpy to GPU_B0
  Do this for every chunk
[Potential] Reconfiguration overhead
  GPU_B7 to register transit buffer with RNIC_B7
  Establish RDMA connection between RNIC_A0 and RNIC_B7

## Slide 35: Why not do it at the application-layer?
Transfer time for 6.4GB KV cache from GPU0 to DRAM0 directly (PCIe) vs. app-driven transit via GPU1.
(whiskers: min, 25th, 50th,75th, and 99th percentiles.)

## Slide 36: Feasibility on existing network infrastructure
Inter-host Network
  Ethernet switches can parse and match on the global device ID
  e.g. src/dest serverIDs as IPv4/6 addresses and the local device ID as IP options
Intra-host Network
  PCIe switches and CPU I/O complex already support routing based on physical memory addresses. Just need to make them runtime programmable.
  PCIe to GPU fabric forwarding: additional hardware support
    Upcoming industry specs like UALink can help standardize this.

## Slide 37: ML workloads driving device-to-device communication

## Slide 38: Forwarding Mechanism
GPU0 writing to DRAM0 indirectly via GPU1

## Slide 39: Training with RNIC Failure
Setup
  GPT2-20B on 4-machines
  32×A100 GPU cluster
  Megatron-LM: TP=2, PP=4, DP=4