## Slide 1: Rearchitecting the TCP Stack for I/O-Offloaded Content Delivery
Taehyun Kim, Deondre Martin Ng, Junzhi Gong*, Youngjin Kwon, Minlan Yu*, KyoungSoo Park
KAIST & *Harvard University
Notes: Hello, I'm Taehyun Kim, thank you for the introduction.
This talk is about a new TCP stack architecture for high performance content delivery.
This is collaboration between KAIST and Harvard University.

## Slide 2: Increasing Demand for High-quality Video Streaming
COVID-19 pandemic (2020~) – “more” rapid increase in video traffic
CDN server performance is critical for cost-effective service
Global Video Traffic
Chart: 
| 항목 1
계열 1 | 90
계열 2 | 119
계열 3 | 156
계열 4 | 201
계열 5 | 258
계열 6 | 326
2017 2022
Exabytes per month
(Cisco whitepaper 2022)
Notes: The demand for higher quality online video streaming keeps on increasing.
Especially during the pandemic, we have seen an explosive increase in video traffic, and the global video traffic is expected to grow as well.
Serving higher quality to a broader population requires lots of resources, so it’s critical to have good CDN server performance for cost-effective operation.

## Slide 3: Computing Hardware Development Trend
2022
1GbE
400GbE
400x
2005
150-200 IOPS
A few 106 IOPS
~104x
2 cores
64 cores
32x
+ Rapid performance improvement with IO devices
- Demise of Moore’s law for CPU advancement (since 2006)
DISK
CPU
NIC
Read()
Send()
Read()
Send()
Video to users
Video to users
Notes: A typical CDN server reads video chunks from disk and serve them to clients via NIC.
Then, which hardware component is a performance bottleneck in modern CDN servers?
About 20 years ago, IO devices such as disk and NIC used to be a typical bottleneck,
but Moore’s law for CPU has ended and there has been revolution in IO device capacity improvement.
For example, the disk bandwidth has grown by 10 thousand times while the NIC capacity has increased by 400 times.
In comparison, CPU improvement for the past two decades is much smaller by a few orders of magnitude.
If the trend persists, CPU is likely to become a performance bottleneck in the near future.

## Slide 4: CPU Consumption for HTTP Video Streaming Server
Typical server operations
  Read an HTTP request
  Read a file chunk for the request
  Send the response
Result
  Observation 1: CPU cycles are 100% utilized
  Observation 2: data plane dominates CPU consumption
Why CPU bottleneck for IO-bound workload?
Benchmark setting
- nginx (v.1.80.0) on Linux
- 300KB files on 4x Optane NVMe
- 100Gbps NIC
- Single core of Xeon Silver 4210
Chart: 
| 항목 1
Disk IO | 33.53
Memory management | 21.93
Network IO | 10.3
File system operations | 6
Control logic | 28.24
Data plane: 72%
Control plane: 28%
Disk IO
Memory
Management
Network IO
open()
fstat()
Application
TCP control logic
Notes: To observe this, we did a simple experiment with an nginx HTTP video streaming server for delivering 300KB video chunks.
We use 4 NVMe disks with a 100Gbps NIC on Linux. This is a complete disk-bound workload.
We observe that over 70% of CPU cycles are spent on data plane operations such as file system operations, disk I/O, and network I/O. In contrast, we find that CPU consumption on the control logic is much smaller.
Why is CPU a bottleneck for IO-bound workload?

## Slide 5: Root cause: “CPU-centric” OS Abstractions
Modern OS designed with “implicit” assumptions
  CPU is fast but IO devices are slow
  CPU is never bottleneck for IO-bound workloads
Artifact: CPU-centric IO operations
  size_t read(fd, buf, size); // DiskMemory
  size_t write(fd, buf, size); // MemoryIO device
  All content must be brought to ”main” memory first!
  Memory (or CPU) becomes the bottleneck
How to avoid CPU bottleneck for IO-bound workload?
Disk
Memory
CPU
Network Card
Notes: This traces back to the very old assumption in operating system design.
In old days, CPU is assumed to be fast while IO devices are slow,
so they assume CPU is rarely a bottleneck for IO-bound workload.
This results in the CPU-centric IO operations. That is, all data in IO devices must be brought to main memory first before running any operations on it.
Read() and write(), and even an optimized API like sendfile() brings the data into main memory first.
However, the old assumption no longer holds. IO devices are getting really fast which makes CPU relatively slow.
Then, the existing design creates a bottleneck in main memory. So, how do we avoid CPU bottleneck for IO bound workload?

## Slide 6: Opportunity in the Solution Space
Modern PCIe devices support P2PDMA
  Peer-to-peer DMA without CPU intervention
  No main memory copy if the DMA devices have memory
Programmability in IO devices
  SmartNICs & computational SSDs
  Arm SOC, FPGA-based, or ASIC-based
Approach: SmartNIC as the hub for NVMe disk IOs
Key design issue: where to place TCP stack?
Disk
Memory
CPU
Network Card
P2P DMA
Notes: In this work, we see an opportunity with peer to peer PCIe DMA.
Instead of reading the content into main memory, why not “NIC” reads it directly from disk via P2PDMA?
Then, we can avoid reading the data into main memory.
Fortunately, modern SmartNIC provides programmability, so we can pull it off.
Then, what happens to the TCP stack? TCP stack is currently run on CPU, but where should it run if NIC directly fetches the content on disk via P2PDMA?

## Slide 7: Challenges in Operating TCP Stack
Option2: TCP stack on SmartNIC
Performance limited by SmartNIC resources
Lighttpd with Linux TCP on Bluefield-2: 12Gbps
  On Xeon Silver 4210: 59Gbps
Hybrid solution?
Separate IO-intensive Data Plane from TCP stack?
Option1: TCP stack on CPU side
No disk content available on CPU
Disk
Memory
CPU
Network Card
P2P DMA
TCP stack
?
?
Notes: The first option is to run the TCP stack on the CPU-side. But the problem is that you cannot create TCP data packets because you don’t have data in the main memory.
OK. The second option is to run the TCP stack on SmartNIC. But then the hardware capacity of the smartNIC is pretty weak.
For example, if you run Lighttpd on Bluefield-2 for video chunk delivery, it achieves only 4.9 times lower throughput than on CPU.
So, we choose the hybrid approach to use both CPU and SmartNIC. We separate IO-intensive data plane from the TCP stack.

## Slide 8: IO-TCP: Split TCP Stack Architecture for Content Delivery
SmartNIC IO-TCP Stack
Host IO-TCP Stack
Reliable data delivery
Congestion control
Flow control
Header generation
Read file from disk
Send packet
Low latency control logic
High throughput data operations
TCP stack
Separation of TCP control/data planes
Notes: IO-TCP, our TCP stack, presents a split TCP stack architecture that addresses the problem.
The key idea is that CPU runs control plane while we offload the dataplane to smartNIC.
The control plane refers to the operations that require low latency control decisions such as reliable data delivery, congestion control, flow control and header generation.
The data plane refers to the other operations that requires high throughput data operations such as disk I/O and data packet I/O. These operations are easily hardwarizable.

## Slide 9: IO-TCP Overview
Client
Provides 4 offload APIs for SmartNIC execution (offload_open(), offload_fstat(), offload_close(), offload_write())
  Application calls offload APIs for remote execution
  Host sends a special command to SmartNIC for each API
  SmartNIC stack performs corresponding IO operations
CPU
NVMe SSDs
Host IO-TCP Stack
Application
Control Plane:
CPU
Data Plane:
SmartNIC & Disk
P2PDMA
Data stream
SmartNIC
SmartNIC IO-TCP Stack
Notes: Here is the overview of IO-TCP.
An application runs on the host stack. When it needs to do IO operations, it can choose to offload the execution of them to SmartNIC.
That is, for file I/O on SmartNIC, the application can call offload_open() and offload_write() to read and send the file content to a client.
For executing the offload operations, the host stack sends a special command to SmartNIC for each operation, and the SmartNIC stack
performs corresponding disk and network I/O operations.

## Slide 10: IO-TCP based Web Server Workflow
Client
CPU
SEND
HTTP
response
body
HTTP
response
headers
OPEN
ACK
Request
ACKs bypass NIC stack
SmartNIC IO-TCP Stack
NVMe SSDs
Host IO-TCP Stack
Application
offload_write()
offload_open()
Control Plane:
CPU
Data Plane:
SmartNIC & Disk
File open/read
via P2P DMA
Notes: Here is the overall operations of an IOTCP-based web server.
When the server receives a request, it opens the corresponding file using offload_open() so that the SmartNIC opens the file from NVMe directly without involving CPU.
When the file is opened, the host stack receives the metadata like the file size from smartNIC, so that the web server can send the response header to the client.
When the application calls offload_write() to send the response body. Then the host stack sends a SEND command packet to the smartNIC stack, and the smartNIC stack reads the file content using P2PDMA and sends it to the client.
When the client sends acknowledgements, they bypass the SmartNIC stack and get delivered to the host stack for executing control logic like congestion control, reliable data transfer, etc.

## Slide 11: Key Operation for Offloading: SEND Command
SmartNIC IO-TCP Stack
Host IO-TCP Stack
Eth
IP
TCP
[‘file id’ ‘offset’ ‘length’]
Eth
IP
TCP
SEND command
(virtual data packet)
SmartNIC HW
TSO
Checksum Offloading
TLS Offloading
Translate the payload of SEND command
Read file asynchronously from disk to the payload
Send out the packet
[‘file id’ ‘offset’ ‘length’]
File
DISK
(real data packet)
Notes: There are four internal commands sent from the host stack to the SmartNIC stack, but I’ll explain only one command, SEND, here.
When the host delivers a SEND command packet to the NIC, the command packet contains the protocol headers of a regular TCP data packet without actual file content in the payload. Instead, the packet payload contains the file id, offset, and length on the payload. So, this is a virtual data packet.
When smartNIC receives the SEND command packet, it translates the given file information, and reads the file content from disk.
And then, it sends out the data packet using scatter gather IO. This is a real data packet.
It also uses standard NIC offload features like TSO, Checksum offloading and TLS offloading.

## Slide 12: IO-TCP Challenges
How to calculate accurate packet RTT ?
How to deal with retransmission ?
Challenges
More details in the paper
Notes: In implementing IO-TCP, we need to address two challenges in making the TCP operations conform to the standard protocol.
The first challenge is how to calculate accurate packet RTT despite of the disk IO delay in the smartNIC stack.
For the time constraints, please refer to the paper for the details
and let me explain the the second challenge this time.

## Slide 13: How to Handle Retransmission?
Re-reading the disk for retransmission could be slow!
Our approach
  Keep the data on NIC memory until the data is confirmed to be delivered (ACK)
  Problem: only Host receives all the ACKs (for control logic)
  Solution: periodic notification of ACKnowledgeD(ACKD) sequence numbers (Host  NIC)
    Required memory size <= window size (e.g., 375MB for 100Gbps NIC with 30ms of average RTT )
SEND
SEND
Retransmission triggered
ACK
ACKD
When unACKDed size > threshold
File
Free ACKDed files
Keep the file
File
Long disk IO
Repeat disk IO?
Host
IO-TCP Stack
SmartNIC
IO-TCP Stack
Client
Notes: The second problem lies in how to handle packet retransmission.
We have CPU handle retransmission, but if we are not careful, it will be very inefficient.
Like this picture shows, SmartNIC could re-read the same content from a disk again just for retransmission.
Instead, we have smartNIC keep the content in memory until it is acked by the other endpoint.
So when the host receives acknowledgements, it periodically informs smartNIC about it, so the smartNIC can discard the content when it's really acked.
Required memory =𝑁𝑒𝑡𝑤𝑜𝑟𝑘 𝐵𝑊×𝑎𝑣𝑔. 𝑅𝑇𝑇
e.g., 375MB for 100Gbps NIC with 30ms of avg. RTT << 16/32GB of BF2 NIC memory
In the normal cases: Network BW x avg.RTT
However, what about the worst cases, no upper bound?

## Slide 14: Implementation
Host stack: extended mTCP to support NIC offload
  1,793 lines of code modification on mTCP
NIC stack: based on NVIDIA Bluefield2 SmartNIC
  1,853 lines of C code
  We implement TSO, scatter-gather IO, and TLS crypto offload
Easy to port existing apps
    open(), fstat() and close()  offload_open(), offload_fstat() and offload_close()
    write()  offload_write()
    Porting Lighttpd server to IO-TCP: ~10 lines of code modification
Notes: We implement the host stack by slightly modifying mTCP, a user-level TCP stack.
We implement the SmartNIC stack as a simple DPDK application.
We added only four offload APIs offload- open(), fstat(), close(), and write(), that implement the function in the SmartNIC stack.
This allows porting pretty easy. We needed only about 10 lines of code modification to port lighttpd to IO-TCP.

## Slide 15: Experiment Setup
Baselines
  Lighttpd on Linux TCP with sendfile() (Kernel version: 4.14)
  Atlas: webserver on kernel-bypass TCP stack with raw disk access [1]
    Buffer-cache-free design
    FreeBSD 1.10 & Chelsio 100Gbps NIC
[1] “Disk|Crypt|Net: rethinking the stack for high-performance video streaming.” SIGCOMM, 2017.
Server
Xeon Silver 4210 @ 2.2GHz, 10 cores
with 128GB DDR4
NVIDIA Bluefield-2 (100Gbps x 2)
Intel Optane 900P NVMe (20Gbps x 4)
Client
2 Clients
Max. 80Gbps
Notes: For our testbed, we use a server CPU, two Bluefield2 SmartNICs and four NVMe disks with 20Gbps each.
Since bluefield2 cannot fully saturate three Intel Optane NVMes due to its weak memory bandwidth, we use 2 NVMes per each SmartNIC for now and the maximum throughput is limited to 80Gbps.
We compare our system to two baselines, Linux TCP with sendfile() and Atlas.
Atlas is an academic webserver on kernel-bypass TCP stack with raw disk access in user level
Please note that it’s not an apples-to-apples comparison because the current version of Atlas can only serve hard-wired contents and it misbehaves with higher load.

## Slide 16: IO-TCP Performance - Plaintext
500KB video file chunks (disk bound)
Lighttpd ported to IO-TCP
IO-TCP achieves Full BW of 4 NVMe disks with a single CPU core
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
IO-TCP | 78.13 | 77.74 | 77.79 | 78.83 | 78.19 | 78.06 | 78.37 | 80.54 | 78.4 | 78.06
LinuxTCP | 12.46 | 23.15 | 31.92 | 40.48 | 45.99 | 50.19 | 53.84 | 55.82 | 56.09 | 56.83
Atlas | 20.265 | 39.95 | 60.407 | 79.873 | 78.974 | 79.993 | 80 | 79.144 | 79.582 | 78.813
78.1
20.3
12.0
56.8
IO-TCP
Atlas
LinuxTCP
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LinuxTCP | 12.46 | 23.15 | 31.92 | 40.48 | 45.99 | 50.19 | 53.84 | 55.82 | 56.09 | 56.83
Atlas | 20.265 | 39.95 | 60.407 | 79.873 | 78.974 | 79.993 | 80 | 79.144 | 79.582 | 78.813
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LinuxTCP | 12.46 | 23.15 | 31.92 | 40.48 | 45.99 | 50.19 | 53.84 | 55.82 | 56.09 | 56.83
78.8
[1] “Disk|Crypt|Net: rethinking the stack for high-performance video streaming.” SIGCOMM, 2017.
Max. throughput of 4 NVMes
Notes: For plaintext 500KB files, Linux TCP cannot saturate 4 NVMe disks even with 10 CPU cores.
Atlas reaches the max performance with only 4 CPU cores.
Our system needs only one host CPU core to saturate 4NVMes.
Since our system offloads high throughput IO workload to smartNICs.
We can say that Atlas works well because the workload size fits the CPU cache size here.

## Slide 17: IO-TCP Performance – TLS
500KB video file chunks (disk bound)
Lighttpd ported to IO-TCP
Cipher mode: AES-GCM 256
IO-TCP still reaches the max throughput for TLS traffic
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
IO-TCP+TLS | 77.41 | 77.52 | 77.61 | 78.07 | 77.79 | 77.55 | 77.9 | 78.74 | 77.44 | 77.93
LinuxTCP+TLS | 6.43 | 12.18 | 17.1 | 22.21 | 26.2 | 30.3 | 33.48 | 34.37 | 34.59 | 37.4
Atlas+TLS | 12.013 | 25.241 | 36.956 | 42.172 | 46.399 | 45.036 | 44.919 | 42.829 | 41.906 | 44.183
77.4
6.4
12.5
44.2
37.4
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LinuxTCP+TLS | 6.43 | 12.18 | 17.1 | 22.21 | 26.2 | 30.3 | 33.48 | 34.37 | 34.59 | 37.4
Atlas+TLS | 12.013 | 25.241 | 36.956 | 42.172 | 46.399 | 45.036 | 44.919 | 42.829 | 41.906 | 44.183
Chart: Number of CPU Cores
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LinuxTCP+TLS | 6.43 | 12.18 | 17.1 | 22.21 | 26.2 | 30.3 | 33.48 | 34.37 | 34.59 | 37.4
IO-TCP
Atlas
LinuxTCP
[1] “Disk|Crypt|Net: rethinking the stack for high-performance video streaming.” SIGCOMM, 2017.
Max. throughput of 4 NVMes
Notes: However, when it comes to TLS traffic which is pretty much standard these days, the benefit of Atlas goes away, because CPU becomes overloaded.
It's inevitable to see the performance degradation in the CPU-centric systems if the workload size exceeds the LLC.
In contrast, IO-TCP still reaches the max performance as it effectively leverages crypto hardware offloading.

## Slide 18: Source of Performance Improvement
Separation of Control plane / Data plane
- No main memory read/write for IO
- No CPU cache eviction by DDIO
Mitigated Cache & Memory contention for Control plane
Separation achieves 27% lower LLC miss rate
Shorter e2e RTT  Larger window size
Overall Throughput Improvement
Chart: Additional Delay by the control plane (μs)
| 10 | 20 | 40 | 60 | 80 | 100
 | 99.1011 | 62.9213 | 37.0787 | 28.0899 | 21.573 | 18.2022
Faster control plane
IPC of the control path improves by 58%
Notes: The IO-TCP throughput is actually higher than that of simply adding the processing power of host CPU and SmartNIC.
Then, why does IO-TCP perform better?
Separating the control and data paths reduces the cache contention of the control logic, and make the execution time of control path much faster.
Then, the faster control plane reduces the RTT and helps increase the send window size faster.
To demonstrate our analysis, we measured the LinuxTCP with extra delay to emulate the LLC misses. We find that even with 20 microseconds of a control path delay, the overall performance was significantly reduced.

## Slide 19: IO-TCP Overhead Evaluation
Overhead factors
  Host-NIC communication overhead
  Performance limit of Arm-based subsystem on BF2
  The fewer connections would be advantageous to CPU-only approach (Linux TCP)
Chart: Number of Connections
| 1 | 2 | 4 | 8 | 16 | 32 | 64
IO-TCP | 4.32 | 8.12 | 17.63 | 22.56 | 26.86 | 30.99 | 36.78
Linux TCP | 6.37 | 9.31 | 9.78 | 9.86 | 10 | 10.08 | 9.99
Chart: Number of Connections
| 1 | 2 | 4 | 8 | 16 | 32 | 64
IO-TCP | 0.44722 | 0.89574 | 1.806 | 2.41 | 2.59 | 2.73 | 2.76
Linux TCP | 0.79 | 1.251 | 1.327 | 1.32 | 1.342 | 1.357 | 1.3244
300 KB files
10 KB files
Notes: You might suspect there's overhead in our system as the host stack needs to communicate to SmartNIC stack for packet transmission.
That's true, so we did some experiments to magnify this overhead.
When the number of connections is small like 1 or 2, Linux TCP outperforms IO-TCP, but when the number of connections becomes 4, IO-TCP is still better.
On the right side, when you deal with a small content like 10KB files, the similar trend happens.
But as long as the number of connections is 4 or larger IO-TCP still performs better.

## Slide 20: Summary
BIG Trend: IO device advancement outpaces the rate of CPU capacity growth
IO-TCP: a split TCP stack architecture for a content delivery system
  CPU host stack carries out the control plane functionalities of a TCP stack
  NIC stack serves as data plane of a TCP stack
IO-TCP achieves full bandwidth of 4 NVMe disks with a single CPU core
  Current bottleneck lies in SmartNIC memory bandwidth
  SmartNIC with higher memory BW will improve the throughput even more
    Bluefield-3 will achieve 140Gbps per NIC
QUIC-based CDN can adopt our separated stack design as well
Notes: In summary, we observe that CPU is becoming relatively more expensive while IO devices are getting faster.
IO-TCP presents a new TCP stack architecture for content delivery that allows harnessing IO device capacity more efficiently with little CPU cycle consumption.
Our prototype shows that one requires only a single CPU core to handle 80 Gbps disk bound workload.
Although the current bottleneck lies in SmartNIC memory bandwidth, SmartNICs with higher memory bandwidth will improve the throughput even more.
For example, Bluefield-3 will achieve about 140Gbps per NIC.
We emphasize that the SmartNIC logic can be easily hardwarizable, and can be made faster, and that our design is general enough to be applied to a related protocol like QUIC.

## Slide 21
Thank you!
Notes: Thank you for listening. I’ll be happy to answer any questions

## Slide 22: IO-TCP Performance – Varying File Sizes
Chart: Plaintext
| 100KB | 300KB | 500KB | 1MB
LinuxTCP | 46.4 | 51.1 | 56.8 | 54.7
Atlas | 78.1 | 79.2 | 78.8 | 79.5
IO-TCP | 64.1 | 76.6 | 78.1 | 75.3
Chart: TLS
| 100KB | 300KB | 500KB | 1MB
LinuxTCP | 28.4 | 33.1 | 37.4 | 36.8
Atlas | 43.4 | 43.8 | 44.2 | 44.1
IO-TCP | 64.1 | 76.2 | 77.4 | 74.8

## Slide 23: IO-TCP Performance – Varying Number of Connections
Chart: TLS
| 1000 | 2000 | 3000 | 4000
1 | 78.25 | 79.33 | 79.04 | 77.43
2 | 79.14 | 79.82 | 79.53 | 80.56
Chart: Plaintext
| 1000 | 2000 | 3000 | 4000
1 | 78.82 | 79.44 | 78.9 | 77.53
2 | 79.07 | 79.96 | 79.65 | 81.51

## Slide 24: Linux TCP vs. IO-TCP
Lighttpd setup | Throughput (Gbps)
Linux TCP on Bluefield-2 only | 11.98
Linux TCP on Bluefiend-2 and 1 CPU core | 22.02
IO-TCP on Bluefield-2 and 1 CPU core | 44.13

## Slide 25: TCP Fairness
Jain’s fairness index with varying number of connections
  IO-TCP: 0.91~0.97
  Linux TCP: 0.90~0.97

## Slide 26: User-level TCP Stacks vs. IO-TCP
Throughput with 500KB file delivery
  TAS: 9.0 Gbps
  mTCP: 21.4 Gbps
  F-Stack: 36.0 Gbps
  Linux TCP: 56.8 Gbps
These stacks are not optimized for large-file content delivery
  Optimized for small messages
  Lacks of an implementation for sendfile() and a support for TSO

## Slide 27: Asynchronous sendfile() on FreeBSD vs. IO-TCP
Chart: Plaintext
| 100KB | 300KB | 500KB | 1MB
FreeBSD-nginx | 34.2 | 60.8 | 67.2 | 70.9
IO-TCP | 64 | 76.2 | 78.1 | 75.3
Chart: TLS
| 100KB | 300KB | 500KB | 1MB
FreeBSD-nginx | 19.2 | 33.9 | 34.8 | 38.8
IO-TCP | 64.1 | 76.2 | 77.4 | 74.8

## Slide 28: Retransmission Timer & RTT Measurement
Client
CPU
SEND
SmartNIC IO-TCP Stack
NVMe SSDs
Host IO-TCP Stack
Application
offload_write()
SEND
ECHO
Disk I/O delay
Retransmission timer at the host stack
  Problem: disk access delay is added
    Up to a few ms when backlogged
  Solution: SEND ECHO packets to the host
    Short & fixed delay (~3us in our setup)
    Negligible overhead: a SEND for 10s~100s MTUs
Short& Static delay
Notes: The first challenge is how to implement the retransmission timer and RTT measurement accurately. When SmartNIC handles SEND message from the host, it needs to read the data from disks, which can take up to a few milliseconds in the worst case. So, the timer could expire prematuraly if we ignore the disk delay.
To address the problem, SmartNIC notifies the host by an ECHO packet when the data packets are really sent out.
Then, the host stack can start the timer for the data packets.

## Slide 29: Retransmission Timer & RTT Measurement
Client
CPU
SEND
SmartNIC IO-TCP Stack
NVMe SSDs
Host IO-TCP Stack
Application
offload_write()
SEND
ECHO
Retransmission timer at the host stack
  Problem: disk access delay is added
    Up to a few ms when backlogged
  Solution: SEND ECHO packet to the host
    Short and static delay (3us in our setup)
    Negligible overhead: a SEND for 10s~100s MTU
RTT measurement with Timestamp option
  Add the static delay(3us) and the I/O delay to the
Notes: The same problem happens to RTT measurement.
To remedy the problem, the smartNIC readjusts the timestamp option value by adding the IO deay and the internal packet transfer delay.

## Slide 30: CPU as a Bottleneck for NVMe
With multiple NVMe disks, CPU can be a bottleneck
  Intel Xeon Silver 4210 (2.20GHz)
  6x Intel Optane 900P
  Simple fio
  A single CPU core cannot even support 2 disks for 4K BS
Chart: Number of NVMe Devices
4K BS | 100 | 100 | 100 | 100 | 100 | 100
8K BS | 89.29 | 100 | 100 | 100 | 100 | 100
16K BS | 57.16 | 98.92 | 100 | 100 | 100 | 100
32K BS | 41.06 | 66.76 | 92.89 | 100 | 100 | 100
64K BS | 31.31 | 45.54 | 56.72 | 73.42 | 88.88 | 100