## Slide 1: DREAM: Dynamic Resource Allocation for Software-defined Measurement
Masoud Moshref, Minlan Yu,
Ramesh Govindan, Amin Vahdat
(SIGCOMM’14)
Notes: Thanks for the introduction.
My talk is about resource allocation for measurement tasks.
This is motivated by the rapid evolution of networks and the need to achieve high levels of performance and availability in networks.

## Slide 2: Measurement is Crucial for Network Management
Heavy Hitter detection
Change detection
Netflix
Expedia
Reddit
Accounting
Anomaly Detection
Traffic Engineering
Heavy Hitter detection
Heavy Hitter detection
Change detection
Change detection
Failure Detection
Accounting
Traffic Engineering
Tenant:
Management:
Measurement:
Network:
Notes: The biggest obstacle to achieving these goals is that our solutions for managing large networks is primitive.
Modern data centers contain many tenants which may wish to perform management tasks such as accounting, failure detection and traffic engineering.
Today, achieving these management tasks in production networks is difficult if not impossible.
We simply do not have visibility into how our networks work.
This makes it harder to introduce new technologies into existing networks, and the "blast radius" from a network failure is often immense. [p]
A big missing component of this larger problem is the ability to measure what is happening inside the network.
These management tasks require concurrent measurements of different types such as finding heavy hitters or large traffic changes.

## Slide 3: High Level Contribution: Flexible Measurement
Management:
Measurement:
Users dynamically instantiate complex measurements on network state
DREAM supports the largest number of measurement tasks while maintaining measurement accuracy,
by dynamically leveraging tradeoffs between switch resource consumption and measurement accuracy
We leverage unmodified hardware
and existing switch interfaces
Network:
Notes: At high level, our contribution is to enable flexible measurements in networks where users can dynamically instantiate a number of complex measurements into the network state.
Our system, DREAM, accommodates the largest number of measurements while maintaining accuracy, by leveraging tradeoffs between aggregate switch resource consumption and measurement accuracy.
Finally, we leverage unmodified hardware and existing switch APIs.

## Slide 4: Prior Work: Software Defined Measurement (SDM)
Controller
Install rules
1
Fetch counters
2
Update rules
3
Source IP: 10.0.1.128/30
#Bytes=1M
Source IP: 10.0.1.130/31
Heavy Hitter detection
Change detection
#Bytes=5M
Source IP: 55.3.4.34/31
Source IP: 55.3.4.32/30
Notes: Prior work has proposed software defined measurement, which permits concurrent measurements by dynamically configuring rules in switches.
For each measurement task, the SDN controller installs one or more rules at switches.
Then switches count traffic associated with the prefixes for the corresponding rules.
In our example, the controller installs a blue rule and a red rule.
Periodically the controller retrieves these counts (in the example, 1Mbytes for the blue rule and 5Mbytes for the red rule).
Finally, the controller can update rules to improve the accuracy of future measurements.
In our example, the controller changes the prefixes associated with the rules.

## Slide 5: Our Focus: Measurement Using TCAMs
Focus on TCAMs enables immediate deployability
Prior work has explored other primitives
such as hash-based counters
Existing OpenFlow switches use TCAMs which permit counting traffic for a prefix
Notes: The focus of our paper is on enabling measurements using TCAMs.
This is because existing OpenFlow switches use TCAMs which permit counting traffic to or from a given prefix.
This choice allows the resulting system to be easily deployable on today’s hardware switches.
Prior work has explored more complicated primitives like hash-based counters which are not available in today’s switches.

## Slide 6: Challenge: Limited TCAM Memory
Controller
Install rules
1
Fetch counters
2
00
13MB
Heavy Hitter detection
01
10
11
13MB
2MB
3MB
Problem: Requires too many TCAMs
64K IPs to monitor a /16 prefix >> ~4K TCAMs at switches
Find source IPs sending > 10Mbps
26
13
13
5
2
3
31
11
10
01
00
Notes: The challenge for using TCAMs is that the number of TCAM entries in switches is limited for power and cost reasons.
We illustrate this using an example measurement task, heavy hitter detection.
Suppose that we are interested in detecting heavy hitters as source IP addresses that send more than 10Mbps.
One way to visualize the traffic from source IP addresses is to use a prefix tree shown on the left.
The numbers inside nodes show the size of their traffic, and the numbers below the leaves show the addresses.
In this prefix tree, we have two heavy hitters in the left subtree.
We can configure rules at switches to monitor all IPs, and periodically fetch counters.
In our example, each switch would have 4 rules, one for each distinct source IP address.
This solution requires too many TCAM entries. [p]
For example, to monitor a large prefix, it needs 64K TCAM entries while today switches have about 4K entries. [p]

## Slide 7: Reducing TCAM Usage
26
13
13
5
2
3
31
11
10
01
00
Monitor internal nodes to reduce TCAM usage
Monitoring 1* is enough
because a node with size 5 cannot have leaves >10
26
13
13
5
2
3
31
11
10
01
00
Notes: We can reduce the number of required TCAM entries by monitoring internal nodes in the prefix tree.
In this example, the right subtree has very little traffic, so monitoring the root of the right subtree is enough.
That node has a total traffic of 5, so none of its leaves can be heavy hitters.
The prefix tree on the bottom shows the updated TCAM configuration: this tree now requires only three TCAM entries.

## Slide 8: Challenge: Loss of Accuracy
Fixed configuration misses heavy hitters as traffic changes
9
4
5
30
15
15
39
26
13
13
5
2
3
31
Missed heavy hitters
Notes: However, keeping the same TCAM configuration over time can result in loss of accuracy because traffic changes with time. The prefix tree on the bottom shows that if traffic changes, our measurement would be unable to detect the two heavy hitters at the leaves of the right subtree.

## Slide 9: Dynamic Configuration to Avoid Loss of Accuracy
9
4
5
30
15
15
39
Find leaves >10Mbps using 3 TCAMs
Divide
Merge
30
15
15
39
9
4
5
Monitor parent to save a TCAM
Monitor children to detect HHs but using 2 TCAMs
Notes: To overcome this loss of accuracy in other words to avoid missing heavy hitters, it is important to dynamically reconfigure the TCAMs as traffic changes.
Previous work has proposed a divide and merge algorithm for this purpose.
We divide the large node and monitor its children to find heavy hitters in the next epoch, but this will use 2 TCAM entries instead of one.
So to save TCAM entries, we merge small nodes and monitor their parent. [p]

## Slide 10: Reducing TCAM Usage: Temporal Multiplexing
# TCAMs Required
Time
Task 1
Task 2
Required TCAM changes over time
Notes: So far we have talked about how to find the right configuration of TCAMs for a single task.
But to support many concurrent tasks, we can use other ideas to efficiently use TCAMs.
This figure shows how many TCAMs are required for heavy hitter detection task over time.
If two tasks have different TCAM requirements at different times, we can use statistical multiplexing to reduce TCAM usage.
For this, we need to dynamically allocate TCAMs and to reconfigure them.

## Slide 11: Reducing TCAM Usage: Spatial Multiplexing
# TCAMs Required
Time
Switch A
Switch B
Required TCAMs varies across switches
Only needs more TCAMs at switch A
Notes: Another idea is based on the observation that some tasks may see traffic at multiple switches.
Because different switches see different levels of traffic, the TCAM required for the task varies across switches.
In this example, the task needs more TCAMs only on switch A.
We can leverage this for spatial multiplexing to reduce TCAM usage.

## Slide 12: Reducing TCAM Usage: Diminishing Returns
Accuracy Bound
12%
7%
Can accept an accuracy bound <100% to save TCAMs
Notes: It is possible to be more aggressive in reducing TCAM usage.
We have found a pattern of diminishing returns in accuracy for many measurement tasks.
In this figure, as we double TCAM entries, the accuracy gain becomes smaller and smaller.
Also the additional heavy hitters detected are small and close to the threshold.
So, we can significantly reduce TCAM usage by keeping task accuracy above a bound that is below 100%.

## Slide 13: Key Insight
Leverage spatial and temporal multiplexing and diminishing returns
to dynamically adapt the configuration and allocation of TCAM entries per task
to achieve sufficient accuracy
Notes: Thus, the key insight in our work is to leverage multiplexing and diminishing returns to dynamically adapt the configuration and allocation of TCAM entries per task to achieve sufficient accuracy.

## Slide 14: DREAM Contributions
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
Supports concurrent instances of three task types: Heavy Hitter, Hierarchical HH and Change Detection
Significantly outperforms fixed allocation and
scales well to larger networks
Algorithm
System
Evaluation
Notes: Given this insight, our paper makes three contributions.
We have designed a system called DREAM that supports three types of measurement tasks: Heavy hitter, hierarchical heavy hitter and change detection.
We have developed algorithms to dynamically adapt TCAM allocations and to dynamically reconfigure TCAMs for tasks over time and across switches while maintaining sufficient accuracy for tasks.
Finally, we demonstrate, using experiments on a prototype and trace driven simulations, that DREAM significantly outperforms alternative schemes such as fixed allocation.

## Slide 15: DREAM Tasks
Heavy Hitter detection
Hierarchical HH detection
Change detection
Anomaly detection
Traffic engineering
Accounting
Network provisioning
DREAM
DDoS detection
Network visualization
Management
Measurement
Network
Notes: Our first contribution is the design of a software defined measurement system called DREAM.
DREAM supports heavy hitter, hierarchical heavy hitter and change detection.
These three task types can cover many management tasks such as Anomaly detection, Traffic engineering and DDoS detection.

## Slide 16: DREAM Workflow
Task Instance 1
Task Instance n
DREAM
SDN Controller
Report
Instantiate task
Configure counters
Fetch counters
  Task type
  Task parameters
  Task filter
  Accuracy bound
TCAM Allocation and Configuration
Notes: Here is how DREAM works from the perspective of the user of the system.
DREAM is a software that runs on an SDN controller.
Users define a task by specifying its type, its parameters, its filter, and an accuracy bound.
Then DREAM creates an instance of this task.
The task instances periodically configure counters, fetch counters and report to the user.
However, at the heart of DREAM are the algorithms for dynamically adapting TCAM allocations and configurations.

## Slide 17: Algorithmic Challenges
How to allocate TCAMs for sufficient accuracy?
Which switches to allocate?
How to adapt TCAM configuration on multiple switches?
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
allocations
sufficient accuracy
allocations
switches
configuration
switches
Diminishing Return
Temporal Multiplexing
Spatial Multiplexing
Notes: There are three challenges in our algorithmic contribution.
The first challenge is how to allocate TCAMs for sufficient accuracy.
The second challenge is to decide which switches to allocate.
The last challenge is given the TCAM allocations, how to adapt TCAM configuration on multiple switches.
I will talk about the first two challenges and for the third, please refer to the paper.

## Slide 18: Dynamic TCAM Allocation
Allocate TCAM
Estimate accuracy
Measure
We cannot know the curve for every traffic and task instance
Thus we cannot formulate a one-shot optimization
We don’t have ground-truth
Thus we must estimate accuracy
Why iterative approach?
Enough TCAMs  High accuracy  Satisfied
Not enough TCAMs  Low accuracy  Unsatisfied
Why estimating accuracy?
Notes: The first challenge is dynamic TCAM allocation.
The general idea behind our algorithm is to iteratively and periodically
(a) estimate the instantaneous accuracy of tasks and
(b) adapt TCAM allocation to keep all tasks satisfied.
In this example, suppose that we have two tasks and have estimated their accuracy.
One with happy face has high accuracy and is rich which means it has enough TCAMs,
and another with sad face has low accuracy and is poor.
In the allocation step, we take resources from the rich task and give to the poor one.
Later when tasks measure using the new allocation and we estimate their accuracy, both tasks become satisfied.
In an earlier slide, we showed the curve of the accuracy of measurement vs. the number of allocated TCAMs.
In general, this curve is not known beforehand, and changes with traffic and the specific parameters of a task.
Thus, it is not possible to formulate a one-shot optimization problem for this.
So, we choose an iterative approach.
Second, we don’t know the current accuracy of a task because we don’t have ground truth.
Thus we must estimate accuracy.
I will now describe each of these components.

## Slide 19: Estimate Accuracy: Heavy Hitter Detection
True detected HH
Detected HHs
Precision =
True detected HH
True detected + Missed HHs
Recall =
Is 1 because any detected HH is a true HH
Estimate missed HHs
Notes: Estimating accuracy depends on the type of a task and here I describe accuracy estimation for heavy hitter detection.
In general, there are two metrics for accuracy: Precision and Recall.
Precision shows how many of detected heavy hitters are true.
But this metric is always 1 for heavy hitter detection algorithm using counters as any detected heavy hitter is a true one.
The other metric, recall, is a measure of the number of missed heavy hitters. In our work, accuracy estimation for heavy hitters estimates recall by estimating the number of missed heavy hitters.

## Slide 20: Estimate Recall for Heavy Hitter Detection
76
26
12
14
5
7
12
2
With size 26: missed <=2 HHs
50
15
35
20
15
0
15
At level 2: missed <=2 HH
Threshold=10Mbps
True detected HH
True detected + Missed HHs
Recall =
Find an upper bound of missed HHs
using size and level of internal nodes
Notes: We find an upper bound for the number of missed heavy hitters using two simple ideas.
To illustrate the first idea, consider the left subtree:
the size of the root is 26, so that subtree cannot have more than two heavy hitters, since our threshold for heavy hitters is 10.
To illustrate the second idea, consider the level 2 node which has a count of 35:
since this subtree has only two leaves, it cannot have more than two heavy hitters.
These two ideas work very well in practice as we show later in our evaluation.
More complicated accuracy estimation ideas for other types of tasks are described in the paper.

## Slide 21: Allocate TCAM
Goal: maintain high task satisfaction
Small  Slow convergence
Large  Oscillations
Time
Accuracy
Time
Accuracy
How many TCAMs to exchange?
Fraction of task’s lifetime with sufficient accuracy
Notes: Now that we know how to estimate accuracy, I describe how to allocate TCAMs:
The goal of our allocation algorithm is to maintain high task satisfaction, where satisfaction is the fraction of task’s lifetime with sufficient accuracy.
In the algorithm, rich tasks offer TCAMs and poor tasks request TCAMs.
But how many TCAMs should be exchanged so that all tasks become satisfied?
In some cases, adding a fixed amount of TCAMs to a task can increase its accuracy in small steps as shown on the left.
This can result in slow convergence, and low satisfaction.
In other cases, adding a fixed amount of TCAMs to a task can increase its accuracy in large steps, resulting in oscillations.
Our approach adaptively changes the exchange step size based on the current accuracy of the task and the details are in the paper [p].

## Slide 22: Avoid Overloading
Not enough TCAMs to satisfy all tasks
Reject new tasks
Drop existing tasks
Solutions
Notes: As TCAMs are limited, it is possible that the system may not have enough resources to satisfy all tasks.
To avoid this, we reject incoming tasks.
However, as the required TCAMs for a task changes overtime, overloading can happen even without accepting a new task.
In this case we drop existing tasks based on assigned priorities.
The paper contains more details like how to detect if the system is overloaded on multiple switches.

## Slide 23: Algorithmic Challenges
How to allocate TCAMs for sufficient accuracy?
How to adapt TCAM configuration on multiple switches?
Dynamically adapts tasks TCAM allocations and configuration over time and across switches,
while maintaining sufficient accuracy
Diminishing Returns
Temporal Multiplexing
Spatial Multiplexing
Which switches to allocate?
Notes: Now that we know how to allocate TCAMs among tasks on a single switch, I will discuss TCAM allocation across multiple switches.

## Slide 24: Allocate TCAM: Multiple Switches
A
B
Controller
Heavy Hitter detection
  Local accuracy is important
  If a task is globally unsatisfied, increasing B’s TCAMs is expensive (diminishing returns)
  Global accuracy is important
    If a task is globally satisfied, no need to increase A’s TCAMs
Use both local and global accuracy
20 HHs
10 HHs
30 HHs
A task can have traffic from multiple switches
Notes: There are many switches in a network, and tasks can have traffic from multiple switches.
Consider a task that has heavy hitters on two switches.
For example, it has 30 heavy hitters, and 20 of them are on switch A and 10 on switch B. How do we determine
(a) whether to increase the number of TCAMs allocated to a task and
(b) which switch or switches to make the increase?
Now, suppose that in our example, the task is globally satisfied, even though it is not satisfied on one of the switches.
In this case, the task does not need additional TCAM entries, even though in switch A its accuracy is not sufficient.
On the other hand, if the task is not globally satisfied, we must increase TCAMs on some switches.
But because of the diminishing returns in accuracy, increasing the accuracy at switch B, which is already satisfied, is expensive.
In the paper, we describe an algorithm that uses both global and local accuracy to decide when and where to adapt TCAM allocations.

## Slide 25: DREAM Modularity
Task Dependent
Task Independent
TCAM Allocation
TCAM Configuration:
Divide & Merge
DREAM
Accuracy Estimation
Notes: Here is how the algorithms fit into the DREAM design.
Dream carefully separates task independent algorithms from the task dependent algorithms.
TCAM allocation and configuration algorithms are task independent:
So when a new task type is added, these algorithms need not be extended.
However, for each new task type, we need to design a new accuracy estimator.

## Slide 26: Evaluation: Accuracy and Overhead
Overhead
How fast is the DREAM control loop?
Accuracy
Satisfaction of a task: Fraction of task’s lifetime
with sufficient accuracy
% of rejected/dropped tasks
Notes: Our evaluation had several goals.
We want to measure the accuracy of DREAM tasks, and DREAMs overhead.
Our evaluation has two main metrics: [p] Satisfaction of a task as the fraction of task’s lifetime with sufficient accuracy.
And percentage of dropped/rejected tasks.
We need this second metric because a scheme can satisfy tasks by rejecting or dropping a large fraction of tasks.
Here, I only show the results for the accuracy of DREAM tasks.

## Slide 27: Evaluation: Alternatives
Equal: divide TCAMs equally at each switch, no reject
Fixed: fixed fraction of TCAMs, reject extra tasks
Notes: We compare DREAM to two alternatives.
Equal allocation divides TCAM entries equally among tasks and does not rejected any tasks.
Fixed allocation allocates a fixed fraction of TCAMs to each task and rejects extra tasks.

## Slide 28: Evaluation Setting
Prototype on 8 Open vSwitches
256 tasks (HH, HHH, CD, combination)
5 min tasks arriving in 20 mins
Accuracy bound=80%
5 hours CAIDA trace
Validate simulator using prototype
Large scale simulation (4096 tasks on 32 switches)
accuracy bounds
task loads (arrival rate, duration, switch size)
tasks (task types, task parameters e.g., threshold)
# switches per tasks
Notes: We evaluate our prototype on 8 switches with single type of tasks as well as combination of them.
We also run trace-driven simulations for large scale scenarios and parameter sensitivity analysis.

## Slide 29: Prototype Results: Average Satisfaction
DREAM: High satisfaction of tasks
at the expense of more rejection for small switches
Average Satisfaction
# TCAMs in Switch
# TCAMs in Switch
Fixed: High rejection as over-provisions for small tasks
Notes: This slide shows the results of an experiment in which we ran a combination of tasks on our prototype and changed the number of TCAMs in the switch.
The diagram on the left shows the average satisfaction of tasks and the right diagram shows the rejection and drop rate.
DREAM has a significantly higher satisfaction rate than alternatives even at low switch capacity where the load is high.
For small switches, this comes at the expense of more rejected tasks.
In comparison fixed and equal allocation could not keep the average satisfaction high for small switches even though fixed allocation rejects a number of tasks.
With increasing switch capacity, DREAM maintains satisfaction but with graceful decrease in the rejection rate.
However, fixed allocation has high rejection rate for large switches because it over-provisions for small tasks.
At low load for large switches, it may appear that fixed and equal perform comparably with DREAM.

## Slide 30: Prototype Results: 95th Percentile Satisfaction
DREAM: High 95th percentile satisfaction
Equal and Fixed only keep small tasks satisfied
95th Percentile Satisfaction
# TCAMs in Switch
Notes: However, when we look at the 95th percentile, rather than the average, the difference between the schemes becomes much more obvious.
For large switches in low loads, DREAM has nearly twice higher satisfaction than Equal or Fixed at the 95th percentile.
Unsatisfied tasks in equal and fixed methods are large tasks, but dream can distinguish large and small tasks using their accuracy estimators and gives them just the right amount of TCAMs.

## Slide 31: Conclusion
Dynamic TCAM allocation across measurement tasks
Diminishing returns in accuracy
Spatial and temporal multiplexing
Future work
More TCAM-based measurement tasks (quintiles for load balancing, entropy detection)
Hash-based measurements
DREAM is available at
github.com/USC-NSL/DREAM
Measurement is crucial for SDN management
in a resource-constrained environment
Notes: In conclusion, the SDN management plane is still in its early stages, and an important part of management is making dynamic measurements in a resource-constrained environment.
Dream addresses the resource allocation problem for TCAM-based measurement tasks in SDN using diminishing returns and leveraging spatial and temporal multiplexing.
DREAM is available at this URL and I’m happy to take questions.

## Slide 32: Related Work
Resource allocation in SDN
  Single switch: FlowVisor, OpenSketch,
  Single task: CSAMP, Volley
  Only controller bandwidth: Payless
Software Defined Measurement
  TCAM-based task implementations
  OpenSketch

## Slide 33: Brief Overview of OpenFlow
Filter
Action
Stats
Priority
Drop packet
Forward packet to port(s)
Forward packet to controller
Packet & byte counters
Among other rules
(a number)
Switch port
MAC src
MAC dst
IP src
IP dst
TCP sport
TCP dport
…
+ MASK
Notes: OpenFlow packets contain a set of rules.
Each rule has a filter part that matches on packet header fields (such as source IP and destination IP) and can use a mask to ignore some fields or bits, for example to match on IP prefixes.
If a packet matches a rule, the switch must apply the specified action. For example drop the packet.
The switch counts the number of packets and bytes matched each rule so that the controller can fetch these statistics for measurement.
Finally, if a packet matches two rules, the switch only applies the rule with the highest priority.

## Slide 34: Avoid Overloading the System
How to calculate headroom?
Strawman 1: Always take additional resources from rich tasks: Could have used resources to cover variations
Strawman 2: Calculate based on summation of steps
  Rich tasks steps – poor tasks steps
  Not accurate: Rich steps could become very small
Solution: Take resources from rich only when necessary
  A phantom low priority task bugs riches for headroom
Admission control
Drop tasks when a switch is overloaded (Not desirable)
Use headroom to handle resource variation and avoid drops
Reject new tasks if headroom is small
Notes: Admitting too many tasks can leave each task with very small resources, thus admission control is necessary.
I can drop tasks based on a priority scheme when a switch is overloaded but this is not desirable
Instead I keep a headroom to handle resource variations and avoid drops, and reject new tasks if headroom is small
But how to calculate headroom.
The Strawman solution 1 is to always take back additional resources from rich tasks and keep a resource pool. However, this wastes the resources that could have been used to cover resource requirement variations.
Another solution is to calculate headroom based on the difference of rich tasks offers and poor tasks requests.
However, this is not accurate as the step size of rich tasks could become very small and does not represent all of what they can offer.
Instead, I make a phantom low priority task on each switch that bugs riches to contribute to headroom.
Now, if any task needs headroom resources it can take it.

## Slide 35: Divide & Merge Algorithm
Divide the node with maximum score
  Score: the accuracy gain of dividing a node
  E.g., for heavy hitter detection: score = counts/level
Merge to free resources with minimum total score
  Reduced to minimum set cover
  Merge if the score of merge < score of divide
Repeat until no node can be divided
Notes: Then the algorithm will be as follows,
It first selects the node with maximum score to divide.
Score is task dependent and shows the accuracy gain of dividing a node. For example for heavy hitter detection the score of a node is its volume over its level in the prefix tree
Then if the divide step needs overloads a resource we must merge. Finding which nodes to merge with minimum total score is equivalent to minimum set cover problem.
If we find a solution with low cost with apply the changes and repeat these steps until no node can be divided.

## Slide 36: Accuracy Estimation: Hierarchical Heavy Hitter Detection
Definition: Longest prefix with large volume after excluding descendant HHHs
62
27
35
7
20
0
7
12
8
15
20
5
15
0
15
0
5
15
5
5
7
8
HHH
Threshold=10
It is still big after excluding descendant HHHs
Notes: Give definition,
And this is example
The red numbers how the weight excluding the descendant HHH

## Slide 37: Accuracy Estimation: Hierarchical Heavy Hitter Detection
Definition: Longest HHH after excluding descendant HHHs
Accuracy estimation challenge:
  The accuracy of an HHH depends on its descendants
62
27
35
7
20
0
7
12
8
15
20
5
15
0
15
0
5
15
5
5
7
8
Monitored
Real HHH
7
12
Threshold=10
Is wrongly detected as HHH
Will not be detected
Is wrongly detected as HHH

## Slide 38: Adapt Offers and Requests for Fast Convergence
Time
Accuracy
Time
Accuracy
Large exchanges
far from sufficient accuracy
Small exchanges
close to sufficient accuracy
Notes: Our solution adapts the number of TCAMs taken from the rich tasks and given to poor ones.
Specifically, if a poor task is far from being satisfied, we allocate large amounts of resources to increase its accuracy in large jumps.
If the task is nearly satisfied, we allocate TCAMs in smaller increments for stability.
The actual algorithm for this is slightly tricky, and is described in the paper.

## Slide 39: TCAM Configuration Across Multiple Switches
26
A
B
C
26
00*
01*
0**
0**
0**
0**
26
13
13
A
B
C
00*
01*
0**
00*
01*
00*
01*
Divide: Requires more TCAMs on a set of switches
Merge: Finds prefixes that cover a set when merge
13
13
Notes: Once a task is allocated TCAMs, these TCAMs must be configured.
We described a divide and merge algorithm to configure TCAMs iteratively.
The challenge now is to generalize this divide & merge across multiple switches.
To understand why this is a challenge, consider the example shown where in the prefix tree, the left node has traffic from switches A and B, and the right node has traffic from switches B and C.
If the task monitors the parent node, it needs one entry on each switch.
However, if it divides and monitors children, it needs TWO entries on switch B.
In general, dividing a node may require additional TCAM entries on a SET of switches.
To counteract this, in the merge step, we must look for mergeable prefixes that maximally cover a set of switches.
In the paper, we describe an algorithm for this.

## Slide 40: Control Loop Delay
Allocation delay is negligible vs. save and fetch delay
Notes: This diagram shows the breakdown of control loop delay when we change the switch capacity.
Allocation delay is negligible comparing to other delays such as saving and fetching rules.

## Slide 41: Parameter Sensitivity Analysis
DREAM can handle different
  accuracy bounds
  task loads (arrival rate, duration, switch size)
  tasks (task types, task parameters ex. HH Threshold)
  # switches per tasks
DREAM is not sensitive to headroom value
Allocating more frequently improves accuracy of tasks
DREAM: High satisfaction and low rejection and drop
Notes: DREAM can work over a large range of parameter values.
For example, if I change the accuracy bound in the range of 60% to 90%, still dream can keep high satisfaction and low rejection and drop.
I tested dream for different task loads by changing arrival rate and duration of tasks and switch capacity.
I tested it for different task types and different task parameter values
And when tasks can have traffic from different number of switches.
By changing the target headroom and frequency of allocation, I found that dream is not sensitive to target headroom value and
Allocating more frequently improves accuracy of tasks.