## Slide 1: Microscope: Queue-based Performance Diagnosis for Network Functions
Junzhi Gong
Joint work with Yuliang Li, Bilal Anwer, Aman Shaikh, Minlan Yu
Notes: [Script] Hi everyone. My name is Junzhi Gong. I am a PhD student from Harvard University. Today I’d like to introduce our project Microscope, which is the [first] diagnostic tool that can zoom into [µs] level events in Network Functions. This is a joint work between Harvard University and AT&T.
This is the [first] diagnostic tool that can zoom into [microsecond] level events in NFV systems

## Slide 2: Network function virtualization (NFV) is popular
User traffic
NAT
LB
Firewall
Deploy
Notes: [script] Nowadays, network function virtualization (NFV) is becoming popular. We see a lot of virtual network functions in industry. For example, there are NATs (Network address translators), Load balancers, Firewalls, and VPNs. They could be developed by different vendors. An ISP like AT&T could collect those network functions, deploy them in the ISP network, and run them in a DAG topology. Finally, it could start to process user traffic.
. As a result, NFV has become popular in both industry and research [1, 9, 38, 48, 49]. For example, Internet Service Providers purchase network function solutions (e.g., NATs, Firewalls, VPNs) developed by different vendors, then run them in chains or DAGs (Directed Acyclic Graph) to serve traffic from various users.
NFVs are VPN, NAT... Show a DAG of these boxes,
Many vendor NFVs … show vendor logos
Many ISPs/clouds use these NFVs, serving users/traffic
Draw real NAT, LB, etc…
Then present vendors
Figures in the center
Then present links by ISP (ATT, version…)
Then present user traffic

## Slide 3: NFV performance is critical
Hardware Middleboxes
Software Network Functions
Deployment: Flexible
Development: Easy for new functionality
Price: Cheaper
Such benefits require NFV to provide good performance
Notes: [YL Script] As network functions transform from hardware [] to [software], NFV brings many benefits, such as flexible deployment, easier development, and cheaper price. [But] [], such benefits [only] come [] with [good] performance, which is critical in the success of NFV, because NFs run in software
[Script] As network functions transform hardware middleboxes into software network functions running in commodity servers, it bring many benefits. It increases the flexibility in network function deployment, it is easy for developers to develop new functionalities, and it reduces the price. However, such benefits ONLY come with GOOD PERFORMANCE, which is critical in the success of NFV. Since NF runs in software, we need to guarantee that NFs achieve high throughput, low tail and average latency, and no packet loss when processing user traffic.
Change the layout (linear, two boxes)
Font bigger
performance, NF deployments should be able to provide per-packet latencies on the order of 10s of µs, and throughput on the order of 10s of Gbps
These operators often face performance problems. In particular, five operators said they have to diagnose 10-100 performance problems monthly, while four of them spend more than 12 hours on performance diagnosis per month.
Merge slide 6 and 8 here, shrink slide 9 and 10 in a sentence here.
Need real performance numbers/story for NFV
Email ATT about why NFV performance is important
Copy from Omid’s slide

## Slide 4: NFV performance problems is common
NFV: High tail latency, low throughput, packet drops …
Many hops: one NF can affect the whole chain
Many networks: ISP, data center, cellular networks …
Surveyed 19 operators
Spend >12 hours on 10-100 performance problems per month
Survey link: https://www.dropbox.com/s/66cp4k3wl8zm0q5/survey.pdf?dl=0
Notes: [YL Script] Unfortunately, those performance requirements are [hardly] achieved in real deployment of NFV. In reality, we see a [lot] of problems in NFV, including high tail latency, low throughput, and packet drops. In addition, usually the length of the NFV topology could be as long as 6-7 NFs, even if only one NF has problem could affect the whole NF chain. Furthermore, current NFV chains appear in different ISP networks, data center networks, as well as cellular networks, and thus almost [every] user traffic will be processed by an NFV chain. As a result, NFV performance diagnosis is critical in the success of NFV. Our survey with 19 network operators show that many operators spend more than 12 hours on 10-100 NFV performance problems per month.
[Script] However, those performance requirements are hardly achieved in real deployment of NFV. In reality, we see a lot of problems in NFV, including high tail latency, low throughput, and packet drops. In addition, usually the length of the NFV topology could be as long as 6-7 NFs, even if only one NF has problem could affect the whole NF chain. Furthermore, current NFV chains appear in different ISP networks, data center networks, as well as cellular networks, and thus almost every user traffic will be processed by an NFV chain. As a result, NFV performance diagnosis is critical in the success of NFV. Our survey with 19 network operators show that many operators spend more than 12 hours on 10-100 NFV performance problems per month.

## Slide 5: Blame games happen upon problems
LB
FW
FW
VPN
NAT
Long tail latency
Vendor:
Bugs in VPN
User:
Input traffic bursts
ISP:
Misconfiguration in FW
User Traffic
No problem found when running VPN alone
No burst found in traffic log
Notes: [YL Script] However, diagnosing performance problems is not straightforward and causes many [] [blame games]. Here is an example of an NFV chain. After seeing a long tail latency problem in the VPN, the operator first suspects that the VPN vendor is the culprit because there could be a bug in the VPN. But after further diagnosis, there is no problem found when running the VPN alone. Then the operator starts to suspect that user traffic is the culprit because it could send traffic bursts. But this is not the case this time. [Finally], the operator finds that the problem is located [] in the [FW], because there is a misconfiguration in FW. In reality, things could be much more complex. When problems happens, there are always such blame games among different parties, including different NF vendors, different operators, and the user traffic.
[Script] However, diagnosing performance problems in NFV is not easy, because there could be blame games when problems happen. Here is an example of an NFV chain. We see a long tail latency problem in the VPN, and the operator will first suspect that the VPN vendor is the culprit because there could be a bug in the VPN. However, after further diagnosis, we found that there is no problem found when running the VPN alone. Then the operator starts to suspect that user traffic is the culprit because it could send traffic bursts. However, this is not the case this time. Finally, we found that the problem is located in the IDS, because there is a bug in IDS.
Let us use an example to highlight these challenges. Suppose we have an NF chain consisting of a Firewall followed by a VPN. Assume that some packets experience long latency at the VPN. Intuitively, operators start by blaming the VPN vendor for the problem. However, no problems are observed when the VPN is run without the Firewall. As a result, operators start to suspect that it is user traffic that is the root cause of the problem. Sometimes bursty traffic may lead to queue buildups at the VPN which results in a long latency. However, this turns out not to be the case this time. Rather, as we find in the end, this problem is caused by a bug in the Firewall that inflates the time it takes to process some flows, resulting in intermittent traffic bursts towards the VPN.

## Slide 6: Goal: Identifying the correct causal relations
LB
FW
FW
VPN
NAT
Performance problems
Low throughput
High tail latency
Packet drops
…
Vendors
Operators
User Traffic
Causal relations?
Parties
Notes: [Script] Therefore, when problems happen in NFV, our goal is to identify the correct causal relations between the correct culprit and the performance problem.
In this paper, we propose Microscope, a performance diagnosis tool that identifies the causal relations in a DAG (Directed Acyclic Graph) of NFs without any knowledge of their implementation
Make it concise based on the paper
Visualize it with two boxes, from which behaviors (parties) to problems

## Slide 7: Diagnosis in NFV is harder
Distributed systems: Requests in O(0-100) ms
NFVs: Packets in O(0-10) µs
NFV performance is sensitive to many µs-level events
  CPU interrupts
  Cache misses
  Traffic bursts
Notes: [YL script] And this is [harder] task than diagnosis in distributed systems. Traditional distributed systems focus on REQUEST latencies, which is usually in millisecond level. But in NFV, we focus on [packet] latencies, which is usually in [microsecond] level. The requirement is much tighter. So many [µs-level] events start to become impactful, in NFV systems, such as CPU interrupts, cache misses, or traffic bursts. These µs-level events make prior solutions ineffective in NFV.
[Script] Diagnosis in NFV systems is harder than that in traditional distributed systems. Traditional distributed systems focus on REQUEST latencies, which is usually in millisecond level. However, when things come to NFV, we must focus on packet latencies, which is usually in [microsecond] level. The requirement is becoming much tighter. As a result, the NFV performance is sensitive to many µs-level events, including such CPU interrupts, cache misses, and traffic bursts. In conclusion, for diagnosis in NFV systems, we have to diagnose how those µs-level events impact NFV performance.
Trends …. comparing distributed system with NFV; comparing past with future.
Killer of microseconds
Compare NFV with distributed systems, from requests to packets, from millisecond to microsecond
In microsecond, fine-time scale events matters, this is new challenge, how to diagnose them
Use figures for CPU, memory, and network

## Slide 8
LB
FW
FW
VPN
NAT
Long tail latency
Misconfig
Events happening in the same time window with problems are root causes
long tail latency
Happen at disjoint time periods!
Time window
VPN
time →
FW
misconfig
queue built-up
noisy events
Prior solution: Time-based correlation (NetMedic)
Notes: [YL Script] Prior solutions use time-based correlations. They assume that events happening in the same time window with the problem are root causes. But this assumption becomes invalid in NFV because of so many µs-level noises. Let’s use the previous example to show this. Here we show a timeline of different events in the above example. In the beginning, a misconfiguration in FW is triggered at this time, so the queue in FW starts to build up. After the queue was built up, the VPN starts to suffer from long tail latency during this time period. In the meanwhile, there were also some irrelevant µs-level noisy events. As we can see, the misconfiguration and the latency problem happen at disjoint time periods. In this situation, it’s really hard to define a fixed time window size. If the time window is too small, we can miss such causal relation between the misconfiguration and the long latency. If the time window is too long, the time window could include a lot of different noisy events, which makes it hard to identify the correct causal relation.
This example shows why diagnosis in NFV is [uniquely] challenging because of the µs-level events. In concrete, there two type of challenges.
[Script] Let’s look at how prior solutions for distributed systems work in face of the new requirement in NFV. Prior solutions usually focus on time-based correlation, which is based on an assumption that, events happening in the same time window with problems are root causes. Let’s go back to this example again. Here we show a timeline of each events in the above example. In the beginning, we found a bug in FW is triggered at this time, and then the queue in FW starts to build up. After the queue was built up, we found that the VPN starts to suffer from long tail latency during this time period. There were also some irrelevant noisy events happening during this time. As we can see, the bug and the latency problem happen at disjoint time periods. In this situation, we can hardly define a fixed size of time windows. If the time window is too small, we can miss such causal relation between the bug and the long latency. If the time window is too long, the time window could include a lot of different noisy events, which makes it hard to identify the correct causal relation.
Use animation, timespan of different events, aligned with example in slide 5.
Show that it is hard to determine the correct time window size
Draw time windows to show that does not work

## Slide 9
Challenge 1: Impact propagates over time
LB
FW
FW
VPN
NAT
Long tail latency
Time
Queue length
Time
Traffic rate / Latency
Traffic rate
Latency
VPN’s traffic rate, latency, and queue length
Burst
Long latency
Burst
Notes: [YL script] The first challenge is that impact can propagate [over time]. In the example, the direct cause of the long latency is, there is a burst arriving to the VPN. Now we show the timeline of traffic rate and latency in the VPN. In the beginning, there is only a low rate of background traffic, and the latency keeps at a low number. However, then the burst arrives during this time, which raises up the latency as well. After the burst ends, the traffic rate keeps at a normal level, but the long latency keeps for a while after the burst. We found that the burst happens during this time, while the long latency happen during this time, which is much longer than the burst. The reason for this lasting impact of burst is shown in the right figure. As we can see, the queue length in VPN starts to grow when the burst arrives, and still keeps at a high level after the burst, because packets in the queue need to take some time to be processed. As a result, the impact in NFV could propagates over time.
[Script] The above example shows some challenges when diagnosing NFV with many µs-level events. Now let’s show those challenges in details. The directly cause of the long latency is, there is a burst arriving to the VPN. Now we show the timeline of traffic rate and latency in the VPN. In the beginning, there is only a low rate of background traffic, and the latency keeps at a low number. However, then the burst arrives during this time, which raises up the latency as well. After the burst ends, the traffic rate keeps at a normal level, but the long latency keeps for a while after the burst. We found that the burst happens during this time, while the long latency happen during this time, which is much longer than the burst. The reason for this lasting impact of burst is shown in the right figure. As we can see, the queue length in VPN starts to grow when the burst arrives, and still keeps at a high level after the burst, because packets in the queue need to take some time to be processed. As a result, the impact in NFV could propagates over time.
Use animation, timespan of different events, aligned with example in slide 5.
Show that it is hard to determine the correct time window size
Draw time windows to show that does not work

## Slide 10
Challenge 2: Impact propagates across NFs
Time
Input rate
Time
Output rate
Misconfig triggered
Misconfig not triggered
Misconfig triggered
Misconfig not triggered
Queue
buildup
Burst
LB
FW
FW
VPN
NAT
Long tail latency
Burst
Misconfig
FW’s input rate and output rate
Notes: [YL Script] The 2nd challenge is that impact can propagate across NFs. Specifically, in the same example, now let’s move our focus to the [firewall]: why the firewall sends the burst. Here are the timeline of input rate and output rate of firewall. In the beginning, the input rate is normal, and the output rate is equal to the input rate. At this time, an instant misconfiguration is triggered by certain flows, which causes the throughput of firewall to a low number. Therefore, even if the input rate keeps the same, the output rate is very small. After the misconfiguration ends, the output rate becomes much higher than a normal value, which sends a burst to the VPN. The reason for the burst is, during the misconfiguration time, the queue is built up with many packets, and after the misconfiguration ends, the firewall sends those packets as fast as possible, which forms a burst. As a result, the misconfiguration in firewall propagates to the VPN, which means the impact can propagate [across NFs].
[Script] Let’s diagnose further in this example about, why the firewall sends the burst. Now we show the timeline of input rate and output rate of firewall. In the beginning, the input rate is normal, and the output rate is equal to the input rate. At this time, an instant misconfiguration is triggered by certain flows, which causes the throughput of firewall to a low number. Therefore, even if the input rate keeps the same, the output rate is very small. After the misconfiguration ends, the output rate becomes much higher than a normal value, which sends a burst to the VPN. The reason for the burst is, during the misconfiguration time, the queue is built up with many packets, and after the misconfiguration ends, the firewall sends those packets as fast as possible, which forms a burst. As a result, the misconfiguration in firewall will propagates to the VPN, which means the impact will propagate across NFs.
Use animation, timespan of different events, aligned with example in slide 5.
Show that it is hard to determine the correct time window size
Draw time windows to show that does not work

## Slide 11: Challenges of diagnosing fine-grained NFV performance
Challenge 1: impact propagation over time
Challenge 2: impact propagation across NFs
Challenge 3: too many root causes for too many victim packets
Notes: [YL Script] In summary, we found that the impact of problems could propagate over time and across different NFs. Besides, another challenge is the large amount of root causes and victim packets, which is hard for operators to focus.
[Script] Here is a summary for the challenges. We found that the impact of problems could propagate over time and across different NFs. There is also another challenge. There could be too many root causes for too many victim packets, which means we could hardly provide a brief diagnosis report.

## Slide 12: Microscope: Use the queue
By tracing back packets in the queue of VPN
  Learn when the traffic burst arrives and affects VPN
By tracing back packets in the queue of FW
  Learn when the FW buffer packets in the queue
  Learn when the FW sends the burst
Time
Queue length
Time
Output rate
Instant bug
Instant bug ends
Queue
buildup
Burst
Even if the impact propagates over time
Even if the impact propagates across NFs
LB
FW
FW
VPN
NAT
Long tail latency
Burst
Bug
Notes: [YL Script] The key insight of our system Microscope, is that the [queue] can reveal all the propagations. In the above example, by tracing back packets in the queue of VPN, we can learn when the traffic burst arrives and affects VPN, even if the impact propagates over time. Also, by tracing back packets in the queue of FW, we can learn when the FW buffer packets in the queue, and when the FW sends the burst. Therefore, we can learn the impact propagation even if it is across NFs.
Now let me introduce our proposed system, Microscope, which leverages the queue to diagnose problems in NFV. We claim that, in the above example, by tracing back packets in the queue of VPN, we can learn when the traffic burst arrives and affects VPN, even if the impact propagates over time. We claim that, by tracing back packets in the queue of FW, we can learn when the FW buffe packets in the queue, and when the FW sends the burst. Therefore, we can learn the impact propagation even if it is across NFs.

## Slide 13: Microscope: Queue based solution
LB
IDS
IDS
VPN
NAT
Microscope runtime:
Collect queuing data
Microscope offline diagnosis
Queuing data
Victim packets/NFs
Local diagnosis
Propagation diagnosis
Pattern aggregation
Notes: Here is the architecture of Microscope. In the runtime, Microscope collects queuing data from the NFV, which could be used to identify victim packets / NFs, and perform diagnosis. After collecting the data and victims, Microscope then performs offline diagnosis for those victims. The diagnosis consists of three steps, including local diagnosis, propagation diagnosis, and pattern aggregation. I will introduce them now.

## Slide 14: Roadmap
Challenge 1: impact propagation over time
  Local diagnosis based on queuing period
Challenge 2: impact propagation across NFs
  Propagation diagnosis based on timespan analysis
Challenge 3: too many root causes for too many victim packets
  Pattern aggregation: use AutoFocus to aggregate diagnosis results
Notes: [Script] Here is the roadmap for how Microscope resolves the challenges. We first show Microscope uses local diagnosis based on queuing period to resolve the first challenge.

## Slide 15: Local diagnosis: Leverage queuing period
f
Victim packet p
p arrives at this time
starts to buffer packets
Queue length of NF f
Queuing Period
Notes: [Script] The first step in Microscope, local diagnosis, performs diagnosis based on queueing period. So what is queuing period? Let’s assume that a packet p is suffering from long tail latency problem at NF f, because there is a long queue in the NF f. We claim that the formation for the long queue is not only due to the current packets in the queue, but also all the history packets starting from the time when the queue just starts to buffer packets, which is at this time point in this figure. Therefore, we define the queuing period in this way, it starts at the time when the queue starts to buffer packets, and ends at the time when the victim packet p arrives.
Make details simpler. Make animations.
Our key insight is that when a packet experiences a long queue, it is not only because of the current packets in the queue, but also because of all the previous packets that contribute to the queue buildup but already get processed. This is to say that if we had fewer packets, the current queue length would be shorter. Therefore, we introduce a queuing period which defines the time period from the time when a queue starts building (from zero packets) to the current time.

## Slide 16: Local diagnosis: Compare traffic rate
Identify if a problem is local or in the upstream
Lower processing rate than expected
↓
local problem
High input rate than capacity
↓
upstream problem
Queuing period
f
Focus on the whole queuing period →
detect the cause even if it does not exist at the current time!
Notes: [Script] So what can we get from the queuing period? Let me show it now. When we see a victim packet having a long latency problem at an NF f, the target of local diagnosis is to identify whether the problem is local or located in upstream network functions. Microscope achieves it my checking the input rate and the processing rate during the queuing period. If the input rate is higher than the traffic capacity of NF f, we then conclude that the problem is located in the upstream. If the processing rate of f is lower than expected, then we can conclude that the problem is local. Note that the rate is computed during the whole queuing period, and thus we can detect the cause (like the burst, or the interrupt) even if it does not exist at the current time!
Q: How to diagnose lasting impact at the local queue? (Challenge 1)
Use architecture figure
Start by saying that, queue builtup is because input rate > processing rate, find out which one is abnormal

## Slide 17: Roadmap
Challenge 1: impact propagation over time
  Local diagnosis based on queuing period
Challenge 2: impact propagation across NFs
  Propagation diagnosis based on timespan analysis
Challenge 3: too many root causes for too many victim packets
  Pattern aggregation: use AutoFocus to aggregate diagnosis results
Notes: [Script] Now let’s look at the second challenge. Microscope runs propagation diagnosis based on timespan analysis to resolve this challenge.

## Slide 18: Propagation diagnosis
Identify which upstream NF is the culprit
  Which NF makes the traffic bursty
A
B
f
source
Timespan of f
Timespan of B
Timespan of A
Time →
Timespan becomes shorter after NF B
  NF B is the culprit
  Based on how shorter the timespan is, we can quantify the impact of NF B
Timespan analysis
  Check what happens to packets in previous hop →
  detect the cause even if it is in different NF!
Notes: [Script] After the first step, if the problem is located in the upstream, we need further diagnosis to find out which upstream NF is the culprit. This step is used to do it. In the first step, we know that the upstream NFs are sending traffic bursts to the victim NF, so in this step, the key question is, which upstream NF makes the traffic bursty. Microscope uses a method named timespan analysis to achieve it. Let’s look at the steps. The following three lines represent the timeline of packets arrival in NF A, B, and f. Assume that packets in the queuing period arrive at f during this time. We then trace back those packets in upstream NFs, and find out that those packets arrive at B during this time period, and arrive at A during this time period. As a result, we can find that, after the processing of B, the timespan of packets become shorter, which means that, packets become more bursty after B. Therefore, NF B is the culprit. Moreover, based on how shorter the timespan becomes, we can quantify the impact of NF B. Using timespan analysis, Microscope can detect the cause even if it is located in different NF.
Remove definition of PreSet
Talk with YUliang

## Slide 19: What if timespan becomes larger after an NF?
A
B
f
source
Timespan of f
Timespan of B
Timespan of A
Time →
C
Timespan of C
B makes the timespan larger
B is not a culprit
B mitigates impacts from A
Notes: [Script] The diagnosis algorithm has several challenges. The first challenge is, what if the timespan becomes larger after an NF during timespan analysis? As shown in the figure, NF B makes the timespan larger, so the timespan in C is similar as that in A, even if A makes the traffic bursty. Microscope handles this situation as follows. First, NF B is definitely not the culprit. Furthermore, because B makes the timespan larger, so it mitigates, or hides the impacts from A. In this situation, A is the not culprit as well because of the help of B.
Give a hint
Do not use bubbles, too small

## Slide 20: How to perform timespan analysis on a DAG?
A
B
f
source
C
Time →
Timespan analysis on each path
Timespan is adjusted for each path
A
B
C
f
Notes: [Script] Second challenge, how to perform timespan analysis on a DAG topology? Previously, we only introduce timespan analysis on a single chain. Things become more complex when the topology is a DAG, because during the queuing period, different packets may come from different paths. Microscope will perform timespan analysis on each path, and the definition of timespan on each NF is adjusted to make it reasonable. Please refer to our paper for more information.

## Slide 21: Recursive diagnosis
A
B
f
source
Timespan of f
Timespan of B
Timespan of A
Time →
Recursive diagnosis on B
Why B makes traffic bursty
B is the culprit
Notes: [Script] Here is the third challenge. Assume that in timespan analysis, we find that B makes the traffic bursty, and we know that B is the culprit. However, the diagnosis does not end here, because we still need to understand why B makes the traffic bursty. Microscope needs to perform recursive diagnosis on NF B to understand it, which means that, we treat B as the victim, and perform local diagnosis on B recursively.

## Slide 22: Roadmap
Challenge 1: impact propagation over time
  Local diagnosis based on queuing period
Challenge 2: impact propagation across NFs
  Propagation diagnosis based on timespan analysis
Challenge 3: too many root causes for too many victim packets
  Pattern aggregation: use AutoFocus to aggregate diagnosis results
Notes: [Script] Now let’s look at the third challenge. Microscope runs pattern agggation to generate a brief diagnosis report.

## Slide 23: Pattern aggregation
Challenge: AutoFocus is MUCH SLOWER when dealing with 12-field tuples
  <Culprit flow 5-tuple, culprit NF> → <Victim flow 5-tuple, victim NF>
…
A long list of causal relations
A short list of causal relation patterns
AutoFocus
Culprit packet/NF → Victim packet/NF
Notes: [Script] After finding out all the causal relations between the culprit and the victim, we find out that there could be a very long list of causal relations. Therefore, the next step of Microscope is to aggregate them into a brief report. Microscope leverages AutoFocus algorithm, which is an algorithm to find the hierarchical heavy hitters in a traffic, to aggregate those causal relations into causal relation patterns. There is a challenge in using AutoFocus here. AutoFocus is usually used to aggregate traffic, where we mainly focus on 5-tuple. However, here each causal relation has as many as 12 fields, which makes the speed of AutoFocus much slower. To address this challenge, Microscope uses an approximation method. You can check our paper for the details of this approximation.
Use figure in architecture. Too wordy.
Move AutoFocus in the figure
Have examples
Remove legend

## Slide 24: Evaluation setup
Inject problems
  Traffic bursts, interrupts, firewall misconfiguration
Compare with NetMedic
  Time-based correlation with the best time window setting
Output
  A ranked list of root causes for each victim packet
Firewall 1
NAT 1
NAT 2
NAT 3
NAT 4
Firewall 2
Firewall 3
Firewall 4
Firewall 5
Monitor
VPN 1
VPN 2
VPN 3
VPN 4
VPN 5
VPN 6
Testbed
  An example NF DAG from E2 [SOSP’15]
  Each NF runs on one VM using DPDK
  Traffic – CAIDA 16
Notes: [Script] Now let’s look at our evaluation. We run an example NF DAG as shown in the figure, which is referring E2 paper in SOSP 15. Each NF runs on one VM using DPDK. We serve CAIDA 16 traffic to our NF DAG. For the problems to be diagnosed, we inject three kinds of problems, including traffic bursts, interrupts, and firewall bugs which can make the processing rate slower when processing certain flows. We compare our Microscope with NetMedic system, which is a typical diagnosis system using time-based correlation. We configure NetMedic with the best time window setting. The output of each system is a ranked list of root causes for each victim packet, and we compare the accuracy of the two system using this output.
Prepare backup slides to show overhead, …

## Slide 25: Microscope has higher accuracy
Overall accuracy across all injected problems
For 89.7% victim packets, Microscope ranks the correct culprit first
For 36% victim packets, NetMedic ranks the correct culprit first
NetMedic fails to find causal relation with fixed time windows
Notes: [Script] Overall, Microscope has much higher accuracy than NetMedic. This figure shows the result. The x-axis represent the cumulative percentage of victim packets, and the y-axis represent the rank of the correct cause for each victim packet. Let’s look at certain points. This point means, for 89.7% victim packets, Microscope successfully ranks the correct cause first. While for only 36% victim packets, NetMedic ranks the correct cause first. We check the results from NetMedic, and observed that NetMedic failed to find causal relations with a fixed time window, because it usually misses the correlation with many noisy events exist in the same time window.
Tell people how to read the figures.
Just show overall.
Need evaluation setup.

## Slide 26: Running Microscope without injecting problems
Setting: We run the DAG of NFs with 80% load
  Let Microscope to detect natural problems
Observations
  21.7% of all victim packets are caused by propagation
  10.9% are caused by at least two-hop propagation
  Impact propagations are common in real NF deployment
Notes: [Script] We also run Microscope without injecting problems to show how it works in natural environment. We serve the NF DAG with 80% load. Here are our observations. There are 21.7% of all victim packets are caused by propagation, and 10.9% of them are caused by at least two-hop propagation. This means that impact propagations are common in real NF deployment, and Microscope is a great tool to detect them.

## Slide 27: Other results
Microscope outperforms NetMedic
  Different burst size
  Different interrupt intervals
  Different level of impact propagation
Pattern aggregation
  Microscope converts 84K causal relations into 80 patterns
Notes: [Script] We show some other evaluation results here. We changed our evaluation settings, and find out that Microscope outperforms NetMedic in different burst sizes, in different interrupt intervals, and in different levels of impact propagation. Microscope also performs good in pattern aggregation. One evaluation shows that Microscope successfully converts 84K causal relations into 80 patterns.

## Slide 28: Conclusion
NFV performance is critical to the success of NFV
Key challenges of diagnosing NFV
  Impacts propagate over time and across different NFs
Microscope
  Leverages queuing period and timespan analysis to understand impact propagations
  Uses AutoFocus to provide a brief diagnosis report
  Achieves much higher accuracy than existing solutions
LB
IDS
IDS
VPN
NAT
FIRST tool focusing on µs-level performance problems
Notes: [Script] Here is the conclusion. We observe that NFV performance is critical to the success of NFV, which means NFV diagnosis is very important. However, we find out that there are key challenges in diagnosing NFV, which is, the impact of problems could propagates over time and across different NFs. We propose Microscope, which leverages queuing period and timespan analysis to understand such impact propagations. It also uses AutoFocus to provide a brief diagnosis report. Our evaluation results show that Microscope achieves much higher accuracy than existing solutions. Microscope is the FIRST tool focusing on µs-level performance problems. We expect that Microscope to be generically useful to other large-scale systems as we get higher speed and lower latency.
Refer to silkroad slide conclusion.
Microscope is the first tool focuses on fine-time scale events diagnosis.
We hope Microscope can be extended and used in other system involving microsecond-level events, as the trend of higher throughput and lower latency in all systems