## Slide 1
Jaqen: A High-Performance Switch-Native Approach for Detecting and Mitigating Volumetric DDoS Attacks with Programmable Switches
Alan Zaoxing Liu
Joint work with Hun Namkung, Georgios Nikolaidis, Jeongkeun Lee, Changhoon Kim,
Xin Jin, Vladimir Braverman, Minlan Yu, Vyas Sekar
Notes: Today I’m going to present our system jaqen on how we can build a high-performance ISP DDoS defense with emerging programmable network hardware.

## Slide 2
DDoS attacks are getting worse
Increasing in volume
Increasing in diversity
Increasing in cost to defend the attacks
2
9/10/2020 U.S. CISA
9/15/2020 Infosecurity
9/16/2020 Neustar
9/3/2020 ZDNet
Notes: Distributed denial of service attacks are on the rise now today. Despite of decades of efforts, we are facing increasing attack risks in terms of volumes, diversity and large capital and operation cost to defend them For example, recent news from infoSecurity, US cybersecurity and infrastructure security agency
So DDoS attacks are really getting worse regardless of the efforts of more than two decades.

## Slide 3
Requirements for DDoS Defense
Performance:
handle large volumes with low latency
Flexibility:
handle diverse attack vectors
Cost-effectiveness:
handle attacks with low capital and operational costs
Notes: In general, DDoS defense have the following three requirements. First of all, we expect the defense system can handle large volumes with low latency, especially not interrupting legitimate traffic. Second, the system needs to be flexible in order to handle many changing attacks. Third, DDoS systems need to optimize their capital and operational costs for the best cost-effective defense, especially for o perators and ISPs.

## Slide 4
Current DDoS Solutions: Middleboxes
Attacker
Hardware appliance
Out-of-band
Detection
Server Clusters
Inflexible, high cost
low performance, high cost
Victims
Slow or inaccurate
E.g., 100 servers for 1000Gbps mitigation. [Security’15]
Can we do better?
Notes: Given all these requirements in mind, existing ddos solutions rely on out-of-band detection, e.g., NetFlow or sFlow based sampling solutions and offline packet analysis for a slow or inaccurate detection. Once attacks are detected, we can some hardware appliances to mitigate the attacks, for example firewalls with certain mitigation rules. However, these hardware appliances are usually fixed-functioned and inflexible with a high buying cost. For example, Arbor network 100K for 10G volumetric attacks.
Alternatively, we can deploy server clusters to mitigate the attacks. These software appliances are flexible but with low performance. For example, a recent NFV-based defense system needs at least 100 commodity servers to handle 1000Gbps attacks. So my question, can we really conduct better DDoS defense in terms of performance, flexibility and cost?

## Slide 5
Trend: Network devices are more programmable
Programmable Switch
Switch ASICs
Increasing in-network programmability in ISP networks
High line-rate performance (e.g., Tbps)
High programmability using high-level language (e.g., P4)
Cost effective with similar cost as traditional switches
Notes: So there are indeed new opportunities here based on the emerging trend. in the networking community/ With the increasing in-network programmability and new devices in the network, large-networks such asISP networks have the new capabilities now and for the foreseen future. For example, programmable switches

## Slide 6
Current DDoS Solutions: Switches for Scrabbing
Scrubbing Center with programmable switches [Poseidon, NDSS’20]
Still need out-of-band detection.
Scrubbing approach adds large latency.
Unscalable mitigation functions (e.g., Server-like SYN Proxy )
Notes: So, there are some recent efforts that tried to explore the potential of programmable switches for DDoS Defense. For example, Poseidon on NDSS’20. They added programmable switches into the scrubbing centers to improve the ddos defense.
However, their approach is not well suited for large-scale defense (ISP-scale) for several reasons.
They still require out-of-band detection which is slow
The scrubbing center requires extensive traffic rerouting that adds large latency.
They ported a few server-based mitigation functions directly to the switches, which have significant security implications. I will show an example in later.

## Slide 7
Opportunity: Programmable ISP Networks for DDoS Defense
DDoS
Internet Service Provider (ISP)
Near the source or victim of the attacks
Provide defense-as-a-service to the clients
Victims
Notes: To fight against the rising DDoS attacks, ISPs become a vantage point as they are usually near the source of the attack or the victim of the attacks for effective defense. And also ISPs have the incentives to provide the DDoS defense as a service to their clients for profit
So today im focusing on ISP-based defense.

## Slide 8
Can we design ISP-based DDoS defense that fully leverages programmable switches?
Notes: So our questions is simple to state:

## Slide 9
Jaqen: Switch-Native DDoS Defense for ISP
DDoS
Victims
Detection + Mitigation integrated “switch-native” solution.
Designed for ISP networks where there are a LOT of switches.
ISP network as a defender
Notes: To answer this question, our vision is a switch-native ddos defense system called Jaqen that turns an ISP network into a defender. No out-of-band detection, no scrubbing centers, no what’s so ever.
Jaqen integrates detection and mitigation completely in the programmable switches and designed for switch-native mitigation efforts towards volumetric attacks.

## Slide 10
Jaqen’s Full Stack Design
DDoS
Victims
1.
Broad-Spectrum Detection
2.
3.
Controller
Dynamic Resource Allocation
Fast On-demand Mitigation
Notes: In jaqen, we have three compoents

## Slide 11
Broad-Spectrum and Always-On Detection
Packet
Parser
…
+
+
+
+
+
Universal Sketches
Attack Signatures
SYN
RST
DNS
NTP
…
…
Attack types
Attack volumes
Unidentified
A wide-spectrum detection of volumetric attacks.
Compact design with future-proof universal sketches.
Detection metric API: Query (proto, func, mode, freq)
e.g., elephant flows, distinct flows, heavy sources, entropy
Notes: In the Detection components, our design leverage universal sketches to estimate a large range of statistics or even unforeseen functions for different flow identities.
In addition to the sketches, we add a few signature counters as a complement
Together, we can estimate various attacks and volumes.
For users, we provide

## Slide 12
Fast On-Demand Mitigation
Detection results
Available resources
Quick resource allocation
(Optimization solver)
Mitigation Modules:
M1, M2, M3, …
Cannot afford preloading all possible mitigation modules.
Notes: Once we have the detection results, along with the network-wide available resources

## Slide 13
Switch-Optimized Mitigation Library
Best-practice mitigation
SYN Cookie/proxy [BSDC’02, RFC4987]
Block-List [WDFIA’07]
Allow-List [WDFIA’07]
ICMP block
DNS filter
…
Switch-optimized library
Sketches
Bloom filters
Counting bloom filters
SYN Proxy with filters
Exact-match table
Rater limiter
…
Preserve O(10 Million) legitimate connections
with O(10 MB) on-switch memory.
Support mitigation strategies on 21 attacks.
Mitigation API
Notes: In designing mitigation modules, we explore a set of best-practice mitigation strategies, extract their workflow as a few key components and redesign each component with efficient probabilistic data structures. Finally, we provide API for each component to help construct mitigation strategies for current and possibly future attacks.

## Slide 14
Switch-Native SYN Proxy
Client
SYN Proxy
Server
SYN
SYN-ACK
w/ cookie
ACK w/ cookie+1
SYN-ACK
SYN
ACK
SYN Cookie & conn table
Verify cookie
Client
Switch
Server
SYN
Error SYN-ACK
w/ cookie
RST
w/ cookie
SYN-ACK
SYN
ACK
Cookie w/o states
Verify cookie +allowlist
SYN Proxy [NDSS’20]
Jaqen SYN Proxy
Seq. # adjustment
Per-conn state!
Notes: Implementing mitigation functions in switches require careful redesign.

## Slide 15
Evaluation – Single Attack
Comparison with Poseidon [NDSS’20].
Single Intel Tofino switch.
40Gbps attack traffic with 2M legitimate TCP connections.
Mitigation with probabilistic data structures is more scalable.

## Slide 16
Evaluation – Dynamic Attacks
6 volumetric attacks (SYN, ICMP, UDP, DNS, NTP, Memcached)
380Gbps total volume, 3.2 Tbps Intel Tofino switch
High detection accuracy and high mitigation effectiveness

## Slide 17
Conclusions
17
ISP DDoS defense compromises performance, flexibility and cost-effectiveness.
Appealing programmable network devices (e.g., programmable switches)
  * High line-rate packet processing
  * Full packet programmability with low cost
      Jaqen: Switch-native DDoS defense for ISP networks
  * Broad-spectrum detection integrated with on-demand mitigation
  * Network-wide resource management
  * Switch-optimized library for best practice mitigation
Contact: Alan Liu
zaoxing@bu.edu
http://zaoxing.github.io/
Notes: On the rise of DDoS attacks today, ISP is a good place to take care of the attacks. However, existing DDoS defense

## Slide 18
Mitigation Strategy Example: SYN Flood
Filtering
Analysis
Update
Notes: For example, using our API, we can construct a sophisticated mitigation strategy for SYN flood.